## Slide 1: Analysis of Forces on Gates used in Fluid Reservoirs
P M V Subbarao
Professor
Mechanical Engineering Department
Design of Safe Gates for Flood Control and More……

## Slide 2: Geometrical Details of a General Inclined Gate

## Slide 3: The Line of Action for Pressure Force
hCP
The line of action passes through the center of pressure CP of the plate.
The resultant force Fpressure acts not through the centroid but below it toward the high-pressure side.

## Slide 4: Gate Shape Vs Pressure Force
hCP
Final formulas must include the shape of the Gate (plate).
Locate centroid of the plate to include the plate shape into analysis
hCG

## Slide 5: Centroid of the Gate
hCP
hCG
Establish an x-y coordinate system in the plane of the plate with the origin at its centroid.
CG
y
x

## Slide 6: An Intrinsic Coordinate System
hCG
Establish an intrinsic coordinate  down from the water surface in the plane of the plate
CG
y
x

dA
hCP

## Slide 7: Total Hydrostatic Force in Intrinsic Coordinate System
hCG
The total hydrostatic force on one side of the plate in  coordinate is given
CG
y
x

dA
hCP

## Slide 8: Force Equation in Intrinsic Coordinate Systems
hCG
CG
y
x

dA
hCP
The remaining integral is evaluated by noticing from Figure that
h =  sin.

## Slide 9: The Force on the Gate in Intrinsic Coordinate System
hCG
is constant along the plate.
Hence Force equation becomes
CG
y
x

dA
hCP

## Slide 10: Key Factors in Reservoir Density Variation
CG
y
x
Temperature:
As temperature decreases, water generally becomes denser, up to about 4°C for fresh water.
TDS/Salinity:
Higher concentrations of dissolved solids increase density, a critical factor in reservoirs with significant inflows of varying chemical compositions.
First level design approximation consideres constant density model.

## Slide 11: Estimation of Pressure Force: Linear variation of Density
hCG
Consider a linear density variation Model as:
CG
y
x

dA
hCP
+

## Slide 12: Estimation of Pressure Force: Constant Density Model
hCG
The centroidal slant distance from the surface to the plate is defined as
CG
y
x

dA
hCP

## Slide 13: The Force on the Gate: Constant Density
hCG
CG
y
x

dA
hCP
CG

## Slide 14: Force on the Gate in Pascal’s Coordinates: Constant Density
hCG
CG
y
x
hCP
Unravel this by noticing that CG sin = hCG, the depth straight down from the surface to the plate centroid. Thus
=
=
CG

## Slide 15: The Force on Gate Constant Density
hCP
hCG
The force on one side of any plane submerged surface in a uniform density fluid equals the pressure at the plate centroid times the plate area!
Independent of the shape of the plate or the angle  at which it is slanted.
=

## Slide 16: Coordinates of Centre of Pressure
hCG
CG
y
x
hCP
(xCP, yCP)
(0,0)
=
To find the coordinates (xCP, yCP), sum moments of the elemental force p dA about the centroid must be equated to the moment of the resultant Fpressure.
The line of action passes through the center of pressure CP of the plate.

## Slide 17: Y-coordinate of CP
hCG
CG
y
x
hCP
(xCP, yCP)
(0,0)

CG
To compute yCP, we must equate
=
=
In intrinsic Coordinates:

## Slide 18: Y-coordinate of CP
The term pay dA vanishes of due to the definition of centroidal axes.
=
Introducing  = CG-y, we obtain
=
=
=

## Slide 19: Mechanical Equilibrium of the Gate
=
Ixx is the area moment of inertia of the plate area about its centroidal x axis, computed in the plane of the plate.
Substituting for F gives the result
=
=
The negative sign in this equation shows that yCP is below the centroid at a deeper level
Again, .

## Slide 20: X-location of CP
The determination of xCP is exactly similar:
=
=
=
=
=
where Ixy is the product of inertia of the plate, again computed in the plane of the plate.
Substituting for F gives
=

## Slide 21: Important Notes on Location of CP
For positive Ixy, xCP is negative because the dominant pressure force acts in the third, or lower left, quadrant of the panel.
If Ixy = 0, usually implying symmetry, xCP = 0 and the center of pressure lies directly below the centroid on the y axis.

## Slide 22: Operation of Gate in A reservoir
CG
CP

## Slide 23: Enhancement of Operational Ease for Gates in A Fluid Reservoir

## Slide 24: Curved Gates for Operational Comfort

## Slide 25: Parallel to Fan type Pressure Forces on Gates

## Slide 26: Analysis of Curved Gates
The resultant pressure force on a curved surface is most easily computed by separating it into horizontal and vertical components.
Consider the arbitrary curved surface sketched in Figure.
The incremental pressure forces are normal to the local area element.
The direction of local force will vary along the surface and thus simple addition is not valid.

## Slide 27: Simplified Analysis of Curved Gates
Simplification of analysis is possible by identification of three different zones of elemental pressure forces.
However, a laborious three-way integration need to be carried out for complete analysis.

## Slide 28: Identification of Different Elemental Pressure Force Zones
Consider a free-body diagram of the column of fluid contained in the vertical projection above the curved surface.
The desired forces FH and FV are exerted by the surface on the fluid column.
Other forces are shown due to fluid weight and horizontal pressure on the vertical sides of this column.
The column of fluid must be in static equilibrium.

## Slide 29: Zonal Analysis of Curved Gates
In the symmetric column bcde, the horizontal components F1 exactly balance and are not relevant to the discussion.
In the lower, asymmetric portion of fluid abc adjoining the curved gate, summation of horizontal forces shows that the desired force FH due to the curved surface is exactly equal to the force FH on the vertical left side of the fluid column.
This left-side force can be computed by the plane surface formula.

## Slide 30: Zonal Analysis of Curved Gates
based on a vertical projection of the area of the curved surface.
This is a general rule and simplifies the analysis:
The horizontal component of force on a curved surface equals the force on the
plane area formed by the projection of the curved surface onto a vertical plane normal to the component.

## Slide 31: Zonal Analysis
Summation of vertical forces on the fluid free body then shows that
The vertical component of pressure force on a curved surface equals in magnitude and direction the weight of the entire column of fluid, both liquid and atmosphere, above the curved surface.
The calculation of FV involves little more than finding centers of mass of a column of fluid.
An integration of the lower portion abc in Figure has a particularly convexing shape.

## Slide 32: Visualization of Force
=
Force Equation can be visualized physically in this Figure as the resultant of a linear stress distribution over the plate area.
This simulates combined compression and bending of a gate (as beam of the same cross section).

## Slide 33: The Mechanical Stresses in the Gate
=
The “bending” portion of the stress causes no force if its “neutral axis” passes through the plate centroid of area.
The “compression” part must equal the centroid stress times the plate area.