## Slide 1: Analysis of Turbulent Boundary Layers
Tiny Vulnerable Zone of Infection & its Effect on Mean Flow…..
P M V Subbarao
Professor
Mechanical Engineering Department
I I T Delhi

## Slide 2: Evolution of Flat Plate Boundary Layer Thickness
The laminar flat-plate boundary layer eventually becomes turbulent at higher values of x.
x

## Slide 3: Evolution of Flat Plate Boundary Layer Thickness
x
There is no unique value for the x-location where this change to occur.

## Slide 4: Evolution of Flat Plate Boundary Layer Thickness
x
With care in polishing the wall and keeping the free stream quiet, one can delay the transition Reynolds number.

## Slide 5: Receptivity of Boundary Layer to Disturbances

## Slide 6: Sketch of transition process in the boundary layer along a flat Plate
A stable laminar flow is established that starts from the leading edge and extends to the point of inception of the unstable two-dimensional Tollmien-Schlichting waves.
Source: Fluid Mechanics for Engineers, A Graduate Textbook, Meinhard T. Schobeiri, 2010.

## Slide 7: Sketch of transition process in the boundary layer along a flat Plate
z
Location 1: Stable Laminar Zone

## Slide 8: Sketch of transition process in the boundary layer along a flat Plate
z
Location 2: Onset of the unstable One -dimensional Tollmien-Schlichting waves.

## Slide 9: Sketch of transition process in the boundary layer along a flat Plate
z
Location 3: Onset of the unstable two-dimensional Tollmien-Schlichting waves.

## Slide 10: Sketch of transition process in the boundary layer along a flat Plate
z
Location 3+: Bursts of turbulence in places with high vorticity

## Slide 11: Sketch of transition process in the boundary layer along a flat Plate
z
Location 3++Intermittent formation of turbulent spots (Horseshoe) with high vortical core at intense fluctuation.

## Slide 12: Hans Albert Einstein (May 14, 1904 – July 26, 1973)
Hans Albert Einstein an avid sailor, frequently taking colleagues and family out for excursions on the San Francisco Bay.
On his many field trips and academic excursions, he took thousands of pictures, many of which he developed himself and presented as slide shows.
In 1988, the American Society of Civil Engineers created the Hans Albert Einstein Award to recognize outstanding achievements in erosion control, sedimentation and/or waterway development.

## Slide 13: Sketch of transition process in the boundary layer along a flat Plate
z
Location 4: Development of unstable, three-dimensional waves and the formation of vortex cascades

## Slide 14: Sketch of transition process in the boundary layer along a flat Plate
z
Zone 5: Coalescence of turbulent spots into a fully developed turbulent boundary layer.

## Slide 15: Sketch of transition process in the boundary layer along a flat Plate
Fully Developed Turbulent Zone
z

## Slide 16: Evolution of Flat Plate Boundary Layer Thickness
Transition begins at some location xcrit, as shown in the figure.

## Slide 17: Transition of Boundary Layer
xcrit is determined by the critical Reynolds number, Rex,crit.
For flow over a flat plate, transition from laminar to turbulent boundary layer occurs when Reynolds number at x exceeds Rex,crit ~ 500,000.
The transition may occur earlier, but it is dependent especially on the surface roughness.
The turbulent boundary layer thickens more rapidly than the laminar boundary layer due to increased shear stress at the body surface.
For typical commercial surfaces and gusty free streams, a more realistic value is

## Slide 18: Turbulent Flat Plate Boundary Layers
Once the surface layer becomes unstable the flow breaks up into random turbulence.
The profile at a particular location is no longer fixed but varies with time.
In this case profiles can only be analysed as time averages with an associated level of turbulence at each height.

## Slide 19: Holistic Picture of Flat Plate Boundary Layer
Velocity profile in a turbulent FPBL is defined using a simplified law
at large values of Rex > 107 , one-seventh-power law:

## Slide 20: Laminar Vs Turbulent Viscosity
Prandtl was the first to present a working algebraic equation of turbulent viscosity that is applied to boundary layer flows.
The model is based on mixing length hypothesis deduced from experiments and is analogous, to some extent, to the mean free path in kinetic gas theory.
Molecular transport
Turbulent transport

## Slide 21: Prandtl Mixing Length Model
The component of the Reynolds stress tensor is function of mixing length as given:
This is the Prandtl mixing length hypothesis.
Prandtl deduced that the eddy viscosity can be expressed as
The turbulent shear stress component becomes

## Slide 22: Estimation of Mixing Length
To find an algebraic expression for the mixing length lm, several empirical correlations were suggested in literature.
The mixing length lm does not have a universally valid character and changes from case to case.
Therefore it is not appropriate for three-dimensional flow applications.
However, it is successfully applied to boundary layer flow, fully developed duct flow and particularly to free turbulent flows.
Prandtl and many others started with analysis of the two-dimensional boundary layer infected by disturbance.
For wall flows, the main source of infection is wall.
The wall roughness contains many cavities and troughs, which infect the flow and introduce disturbances.

## Slide 23: Quantification of Infection by Seeing the Effect
Develop simple experimental test rigs.
Measure wall shear stress.
Define wall friction velocity using the wall shear stress by the relation
Define non-dimensional boundary layer coordinates.

## Slide 24: Approximation of velocity distribution for a fully turbulent 2D Boundary Layer

## Slide 25: Approximation of velocity distribution for a fully turbulent 2D Boundary Layer
For a fully developed turbulent flow, the constants are experimentally found to be =0.41 and C=5.0.
Laminar Sub Layer
Turbulent (logarithmic)Layer
Intermediate Layer

## Slide 26: Measures for Mixing Length
Outside the viscous sublayer marked as the logarithmic layer, the mixing length is approximated by a simple linear function.
Accounting for viscous damping, the mixing length for the viscous sublayer is modeled by introducing a damping function D.
As a result, the mixing length in viscous sublayer:
The damping function D proposed by van Driest
with the constant A+ = 26 for a boundary layer at zero-pressure gradient.

## Slide 27: Computational Analysis of BL on A Flat Plate
Evolution of Velocity Profiles on a long Flat Plate with

## Slide 28: Summary of Engineering Relations for A FPBL

## Slide 29: Summary of Engineering Relations for A FPBL
The integrated average skin friction coefficients for one side of a flat plate of length L.
The Cf,L applicable to the entire plate from x = 0 to x = L.
For Laminar Flow Region:
For Turbulent Flow Region:

## Slide 30: Turbulent Flat Plate Boundary Layers with wall Roughness:
For fully turbulent rough plate: