## Slide 1: Betz Analysis of Wind Turbines
P M V Subbarao
Professor
Mechanical Engineering Department
I I T Delhi
Scientific Modelling for Guaranteed Power…

## Slide 2: The Power in the Wind
The power in the wind is proportional to:
  the area of windmill being swept by the wind
  the cube of the wind speed
  the air density - which varies with altitude
The formula used for calculating the power in the wind is shown below:
where, P is power in watts (W)
ρ is the air density in kilograms per cubic metre (kg/m3)
A is the swept rotor area in square metres (m2)

## Slide 3: Who are Contiguous to A Wind Turbine?

## Slide 4: Support from Surroundings of A Donating Stream Tube
Arotor
The Mach number is small and the air density is thus constant and the axial velocity must decrease continuously from Vo to u1.

## Slide 5: Thermodynamic Description of Flow Past A Working Wind Turbine
Front view of Stream Tube for HAWT
The rotor disc acts as an energy extractor slowing the wind speed from V0 far upstream of the rotor to u at the rotor plane and to u1 in the wake.

## Slide 6: Basic Assumptions to Identify the Important Design Parameter: Betz
This analysis uses the following assumptions:
Homogenous, incompressible, steady state fluid flow;
No frictional drag;
An infinite number of blades;
Uniform thrust over the disc or rotor area;
A non–rotating wake;
The static pressure far upstream and far downstream of the rotor is equal to the undisturbed ambient static pressure

## Slide 7: Conservation Mass Across Double Boundaries
The conservation of mass for the donor CV gives a relationship between A and A1 as:
The conservation of mass for entire participating wind (outer CV):

## Slide 8
Axial Momentum Balance for an Ideal Wind Turbine
The axial momentum equation using the simplified assumptions of an ideal rotor in a control volume
Rate of momentum entering the Outer boundary:
Rate of momentum Leaving the Outer boundary:

## Slide 9
Donor Wind stream needs to satisfy:
Axial Momentum Balance for an Ideal Wind Turbine
Thrust (T) generated by the wind turbine on wind = Change in Rate of Momentum

## Slide 10: Velocity & Pressure Field Generated in the Donor Stream
Axial Force Generated by Pressure filed on the Wind Turbine

## Slide 11: Stable Operation of Wind Turbine
For Stable operation of wind turbine structure the Axial Force must equal and opposite to Thrust

## Slide 12
It is seen that the velocity in the rotor plane is the mean of the wind speed Vo and the unused wind speed in the wake u1.
Axial Momentum Balance for an Ideal Wind Turbine

## Slide 13: Characteristic Design Parameter of A Wind Turbine Rotor
Define a design parameter as axial induction factor:

## Slide 14: First Law Analysis of SSSF past a Wind turbine
There is no heat transfer across the boundary of CV.
First Law :

## Slide 15: Frictionless Low Mach Number Flow Past a WT
SSSF: Conservation of mass
The flow is assumed to be isothermal, frictionless, no change in potential energy.
SSSF: First Law:

## Slide 16: Power Generated by an Ideal Wind Turbine
The available power in a cross-section equal to the swept area A by the rotor is:

## Slide 17: Non-dimensional Capacity Factor
The absorbed power is often non-dimensionalized with respect to Pavail as a power coefficient CP:
Similarly, a thrust coefficient CT is defined as:
the power and thrust coefficients for the ideal wind turbine using 1-D analysis may be written as:

## Slide 18: The Compact Ideal Wind Turbine
a
Cp
CT

## Slide 19: Maximum Feasible Axial Induction
Differentiating CP with respect to a yields:
It is easily seen that CP, max = 16/27 for a = 1/3.
This theoretical maximum for an ideal wind
turbine is known as the Betz limit (59.3%).

## Slide 20: Actual Performance of WTs

## Slide 21: Wind Turbine : Actual Power Extraction Analysis

## Slide 22: Discussion of Betz Anlaysis
Experiments have shown that the assumptions of an ideal wind turbine (in agreements with Betz thrust equation are only valid for an axial induction factor, a of less than approximately 0.4.
If the momentum theory were valid for higher values of a, the velocity in the wake would become negative as can readily be seen by equation

## Slide 23: The Measured CT as a function of the a

## Slide 24: Construction of Stream Tube
For Ideal Flow:

## Slide 25: Structure of Wake Vs Capacity of A Wind Turbine

## Slide 26: Turbulent-wake state
Induced by the unstable shear flow at the edge of the wake

## Slide 27: Domain of Invalidity of Betz Theory
For a wind turbine, a high thrust coefficient CT, and thus a high axial induction factor a, is present at low wind speeds.
The simple momentum theory is not valid for values of a greater than approximately 0.4.
The reason is that the free shear layer at the edge of the wake becomes unstable when the velocity jump V0 – u1 becomes too high.
This instability leads to formation of eddies, which transport momentum from the outer flow into the wake.
This situation is called the state of Turbulent-Wake.

## Slide 28: State of Turbulent wake

## Slide 29: Optimum Available Power due to Non-ideal Wake
Fraction of Betz Limit

## Slide 30: Creative Designs