## Slide 1: Design of Centrifugal Pumps
P M V Subbarao
Professor
Mechanical Engineering Department
A Popular Liquid Lifting Device……

## Slide 2
General Layout of A Pump

## Slide 3: 21st Century View of Developments in Pumps
The escalating environmental issues driven by energy consumption have underscored the urgent need to enhance energy efficiency across critical sectors.
As widely used general-purpose power machinery, centrifugal pumps account for substantial energy consumption, making their efficiency improvement highly significant.
With societal progress and the rising safety standards, pump design has evolved into a highly complex optimization problem.
PO is characterized as multi-objective, multi parameter, and multi-component integration under nonlinear and strongly constrained conditions.
Key challenges in this field include accurately predicting hydraulic performance and efficiently solving high-dimensional, nonlinear optimisation problems.

## Slide 4
Layout of A Our Pump Test Rig

## Slide 5: Variation of Absolute Pressure inside A Pump
Flow Path
pabsolute

## Slide 6: Available Suction Pressure At a Site
Kinetic power mVs2/2
Frictional loss in suction piping

## Slide 7: Definition of Net Positive Suction Head
NPSH
NPSH is one of the most widely used and least understood terms associated with pumps.

## Slide 8: Loss of NPSH

## Slide 9: Strategies for Pump Erection

## Slide 10
Power Consumed by A Pump

## Slide 11: Cavitation
As the liquid flows onto the impeller of the pump it is accelerated and initially its pressure falls (Bernoulli).
The pressure subsequently increases as the fluid leaves the impeller and as the kinetic energy is recovered in the volute chamber.
If the pressure of the liquid falls below the vapour pressure, pv, the liquid boils, generating vapour bubbles or cavities-cavitation.
The bubbles are swept into higher pressure regions by the liquid flow, where they collapse creating pressure waves and cause mechanical damage to solid surfaces.
Moreover, pump discharge head is reduced at flow rates above the cavitation point.
Operation under these conditions is not desirable and damages the equipment.

## Slide 12: Cavitation regions in An Impeller

## Slide 13: NPSH (Net Pressure Suction Head)
Net Positive Suction Head Required, NPSHr
Understanding the significance of NPSH is very much essential during design stage of the pumps.
Pumps can pump only liquids, not vapors!!!
Rise in temperature and fall in pressure induces vaporization
NPSH as a measure to prevent liquid vaporization
Net Positive Suction Head (NPSH) is the total head at the suction flange of the pump less the vapor pressure converted to fluid column height of the liquid.

## Slide 14: Learnings from Machine: NPSHr is a function of pump design
NPSH required is a function of the pump design and is determined based on actual pump test by the vendor.
As the liquid passes from the pump suction to the eye of the impeller, the velocity increases and the pressure decreases.
There are also pressure losses due to shock and turbulence as the liquid strikes the impeller.
The centrifugal force of the impeller vanes further increases the velocity and decreases the pressure of the liquid.
The NPSH required is the positive head in meters absolute required at the pump suction to overcome these pressure drops in the pump and maintain the majority of the liquid above its vapor pressure.
The NPSH is always positive since it is expressed in terms of absolute fluid column height.
The term "Net" refers to the actual pressure head at the pump suction flange and not the static suction head.

## Slide 15: Learnings from Machine: NPSHr increases as capacity increases
The NPSH required varies with speed and capacity within any particular pump.
The NPSH required increase as the capacity is increasing because the velocity of the liquid is increasing, and as anytime the velocity of a liquid goes up, the pressure or head comes down.
Pump manufacturer's curves normally provide this information.
The NPSH is independent of the fluid density as are all head terms.
Note: It is to be noted that the net positive suction head required (NPSHr) number shown on the pump curves is for fresh water at 20°C and not for the fluid or combinations of fluids being pumped.

## Slide 16: Net Positive Suction Head available, NPSHa
Net Positive Suction Head Available is a function of the system in which the pump operates.
It is the excess pressure of the liquid in feet absolute over its vapor pressure as it arrives at the pump suction, to be sure that the pump selected does not cavitate.
It is calculated based on system or process conditions

## Slide 17
Net Positive Suction Head available, NPSHa

## Slide 18
Erection of Pump
ps
Hs

## Slide 19
Suction Velocity:
Learnings from Machine: NPSHr is a Function of Pump Design

## Slide 20: Control of NPSHr: Geometric Details of Impeller

## Slide 21
Power Developed by A Pump

## Slide 22
Shaft Diameter,d
Hub Diameter,dh
Torque on Pump Shaft:
Suction Diameter:
Geometric Details of Inlet Section of Impeller

## Slide 23
Impeller Inlet Diameter:
Height of Vane at the Impeller inlet:
Impeller Exit Diameter:
Geometric Details of Inlet Section of Impeller

## Slide 24
Pump Shape Factor:
Pump Speed Factor:
Pump Capacity Factor:
Geometric Details of Exit Section of Impeller

## Slide 25
Geometric Details of Impeller Vanes

## Slide 26
Va1
Vr1
Va2
Vr2
Vf2
Vw2
Impeller Velocity Diagrams
b2 : 240 -- 280

## Slide 27: Types of Vanes
Va2
Vr2
Va2
Vr2
Va2
Vr2

## Slide 28
Exit Blade angle of the Impeller b2
Backward Vanes
Radial Vanes
Forward Vanes
Types of Vanes

## Slide 29: Construction of Vane Shape

## Slide 30: Vane Shape for Better Performance
Vf1-2
Vr1-2
b1-2
Vr

## Slide 31: Design of Pump Casing
Volute casing
Volute Diameter at 3600: D3

## Slide 32
Volute width b3 : 1.75 to 2.0 times the exit width of impeller
Volute radius:
Design of Pump Casing

## Slide 33: Performance Parameters
Differential head of pump:

## Slide 34
Pump Curves @ constant Speed

## Slide 35: Variable Speed Operation
, CH = head coefficient
, CQ = flow coefficient

## Slide 37
Head Vs Flow Rate & Selection of Operating Point

## Slide 38
PUMPS Running Parallel