## Slide 1: Sustainable Power Generation Systems for Future
Utilization of Low Quality Sources ……
P M V Subbarao
Professor
Mechanical Engineering Department

## Slide 2: Comparison of Life-Cycle Emissions
Tons of Carbon Dioxide Equivalent per Gigawatt-Hour

## Slide 3: Sustainable Ideas
Several ideas have recently been investigated in an attempt to enhance the utility of low-quality energy resources.
The performance of radial turbines using special phase change working fluids had made it feasible.
Design for phase change liquid instead of water!!!!
Waste will be a Resource …..

## Slide 4: Potential sources with Low Carbon Foot Print
It is a novel idea to find a renewable source to generate green power using Organic working fluid.
The burgeoning world demand cannot be met without utilizing all available sources.
The main sources of utility are as follows:
Geo-thermal
Solar thermal
Biomass
Municipal waste
Main deficiency of these resources is that they cannot generate High temperatures.

## Slide 5: Existing biomass capacity in India
C

## Slide 6: Geo-thermal Map of India

## Slide 7: Few Low Temperature Resources and Their Capacities

## Slide 8: Negative Characterstic of Steam
Pressure, MPa
x
Why should an isentropic expansion lead to condensation???
This demands high Live steam temperature
Tmax = 546C &Tmin=40 C

## Slide 9: Characterization of Vapour Domes for Engineering of Rankine Cycle

## Slide 10: Organic Rankine Cycle
The Organic Rankine Cycle (ORC) uses an organic fluid instead of water.
The selection of working fluids and operation conditions are very important to system performance.
The possibility to select the best working fluid depending on the available heat source and the plant size results in multiple advantages:
(i) more efficient turbomachinery,
(ii) limited vacuum at condenser and
(iii) higher performance compared to both steam Rankine cycles and gas cycles especially for heat sources lower than 400°C and power output lower than 20 MW.

## Slide 11: Classification of Working Fluids for Power Generation
Basically, the working fluid can be classified into three categories.
Dry, isentropic, and wet depending on the slope of the T–S curve (dT/dS) to be positive, infinite, and negative, respectively.
The working fluids of dry or isentropic type are more appropriate for ORC systems.
This is because dry or isentropic fluids are superheated after isentropic expansion, thereby eliminating the concerns of impingement of liquid droplets on the turbine blades.
Moreover, the superheated apparatus is not needed.

## Slide 12: Selection of Working Fluid
Working fluids can be selected from a long list of candidates including
hydrocarbons,
hydrofluorocarbons,
siloxanes and
mixtures of these components.
The distinctive characteristics make ORC the most reliable option for unconventional heat sources like
geothermal brines,
biomass combustion,
waste heat recovery from industrial processes and
thermal solar applications.

## Slide 13: Library of Cycles

## Slide 14: Working Fluids for Low Temperature Resources
Organic Substances must be selected
in accordance to the heat source
temperature level (Tcr < Tin source)

## Slide 15: World Installed Capacity of ORC Plants : per application

## Slide 16: World Installed Capacity of ORC Plants : per manufacturer

## Slide 17: ORC Geothermal : Market share and per manufacturer

## Slide 18: ORC Biomass : Market share and per manufacturer

## Slide 19: ORC Waste Heat Recovery : Market share and per manufacturer

## Slide 20: Evolution of installed capacity : per application

## Slide 21: Evolution of installed capacity : per application

## Slide 22: Gram Swaraj : A pivotal concept in Mahatama Gandhi's thinking
The fundamental concept of Gram swaraj is that every village should be its own republic,
"independent of its neighbours for its own vital wants and yet interdependent for many others in which dependence is necessary," according to Gandhi, writing in 1942.
Each village should be basically self-reliant, making provision for all necessities of life - food, clothing, clean water, sanitation, housing, education and so on ….
Micro Energy Systems are the Requirement of Gram Urjha Swaraj……

## Slide 23: Micro Sized ORC Plants

## Slide 24: Micro Sized ORC Plants

## Slide 25: Micro Sized ORC Plants

## Slide 26: Methodology for Organic Working Fluid Selection : Thermodynamic Factors

## Slide 27: Methodology for Organic Working Fluid Selection : Critical Points

## Slide 28: An Exclusive Working Fluid : R245fa
1,1,1,3,3– Penta-fluoro-propane.
CF3CH2CHF2
Molecular weight : 134.05
Critical Temperature : 427.2 K
Critical Pressure : 3640 kPa
This is a non-ozone depleting working fluid.

## Slide 29: Simple Organic Rankine Cycle
3
4

## Slide 30: T-s Diagram for ORC with Dry Working Fluid

## Slide 31: Methodology to evaluate Cycle Pressure
Estimate maximum possible TIT thru a known source.
Select an initial pressure.
Note local ambient conditions.
Mean effective temperature of heat addition for equivalent isothermal process or entropy averaged temperature is calculated using
Mean Effective Temperature of heat rejection for equivalent isothermal process is calculated using

## Slide 32: Methodology to evaluate Cycle Pressure
Calculate the efficiency
Repeat steps above for pressures varying from 2-20 MPa at 0.5 MPa intervals
Calculate slope of efficiency at various pressures.
The minimum pressure suitable for operation is taken when

## Slide 33: Performance of ORC : Efficiency vs. Pressure for R227ea

## Slide 34: Selection of Pressure for a Working Fluid
Methane | Too low | 2-Methylpentane | 3
Butane | 8 | Heptane | 2
Isobutane | 9 | Octane | 2
2-Methylbutane | 5 | Ethane, pentafluoro- (R125) | 18.5
2-2 Dimethylpropane | 9 | Ethane, 1,1,1,2-tetrafluoro- (R134a) | 10
Hexane | 2 | 1,1,1,2,3,3-Hexafluoropropane (R236ea) | 10.5
Ethane, 1,1,1-trifluoro- (R143a) | 17.5 | Dodecafluoropentane | 8
1,1,1,2,3,3,3-Heptafluoropropane (R227ea) | 15.5 | 1,1,1,3,3-Pentafluoropropane (R245fa) | 8
Decafluorobutane | 11 | Ethane, 1,1-difluoro- (R152a) | 13

## Slide 35: Performance of ORC : Efficiency

## Slide 36: Performance of ORC : Compact Ness

## Slide 37: T-s Diagram for ORC with Dry Working Fluid

## Slide 38: Regenerative ORC
3

## Slide 39: Better Utilization of Low Quality Resources