## Slide 1: A Novel Conservation Variable for Ideal Turbo Machines
P M V Subbarao
Head & Professor
Mechanical Engineering Department
Conservation Variable for Design Principle for Turbomachines !!!

## Slide 2: An Essential Action Across of A Fluid-machine
A Turbomachine
Fluid in
Fluid out

## Slide 3: Read Through Euler Turbo-machinery Equation: Axial Flow:
A Change in methalpy is proportional to change rate of angular momentum.
For machines with little change in mean radius (inlet to exit), the change in methalpy is due to change in tangential flow velocity of the fluid.
Can Create a small change in enthalpy of fluid.
Higher the speed of a turbomachine, higher will be the change in methalpy.

## Slide 4: Read Through Euler Turbo-machinery Equation: Radial Flow
For turbomachines with large change in radius (inlet to exit), the change in methalpy is to a large degree due to the change in radius.
The centrifugal/centripetal effect.
Creates Large change in enthalpy of fluid.
How to select a suitable type of action for a resource/demand.

## Slide 5: The Side Effect: Axial Momentum Equations
Axial Momentum Equation:
A turbomachine cannot tolerate this force doing any work.
The axial force should be completely absorbed by a thrust bearing.
Any remaining traces of this force can cause mechanical or aerodynamic damages.

## Slide 6
What is the Signature of flow along meridional plane in an Isentropic Turbomachine?
An ideal (isentropic) turbomachine must conserve an unknown parameter!!!???!!!

## Slide 7
For an isentropic Turbomachine:
Fusion of Euler and SSFS Equations
On meridional plane of an ideal turbomachine blade along flow direction Rothalpy remains constant

## Slide 8: Conservation of Rothalpy
A cornerstone of the analysis of steady, relative flows in rotating systems has, for many years, been the immutable nature of the fluid mechanical property rothalpy.
"In a moving passage the rothalpy is therefore constant provided:
  the flow is steady in the rotating frame;
  no friction from the casing;
  there is no heat flow to or from the flow.

## Slide 9: Novel Idea for Creation of Variety
Ideas for creation of a variety in turbo-machine.
Through flow Theory

## Slide 10: Blade Velocity Vs Tangential Component of Fluid Velocity
Ub
Ub
Vwi
Vai
Vfi
Vri
In maridional plane at mean radius of rotor
Through Flow Theory

## Slide 11: Rotor Speed Vs Whirl Velocity
Ub
Vwi
Vai
Vfi
Vri
Ub
Vwi
Vai
Vfi
Vri
Vwi
Ub
Vai
Vfi
Vri

## Slide 12: Relative Whirl Velocity
Constant in an ideal turbo-machine

## Slide 13: Stator & Rotor
For stator Ublade =0
For rotors :
For a true axial flow machines: Ublade constant

## Slide 14: Complex Geometrical Features of A Turbomachine

## Slide 15: Throughflow Analysis of Incompressible Turbomachinery
A turbomachine working with incompressible fluid will be isothermal and hence U(T) is constant throughout the machine.
For an Ideal Hydro Turbomachine :

## Slide 16: Conservation of Rothalpy
Ideas for creation of a variety in turbo-machine.
Throughflow Theory