## Slide 1: Advanced Method for Estimation fo EFFECTIVE THERMAL CONDUCTIVITY OF A PCB
Creation of Fast and Accurate Models
P M V Subbarao
Professor
Mechanical Engineering Department

## Slide 2: Fraction of Heat Transferred to/thru PCB

## Slide 3: Transformation of PCB
https://www.heatsinkcalculator.com/blog/how-to-calculate-the-thermal-resistance-of-a-pcb/

## Slide 4: Thermal Resistance Network
The outer portion of each layer is an annulus (referred to as the “outer annulus”) with inner and outer radii rinner and router respectively.
The calculation for ho,n is developed with the approximation that the temperature difference between the layers of the PCB is small.
In reality, the flow of heat is predominantly radial in the outer annulus.
The resistance to heat flow in the outer annulus can then be approximated by the thermal resistance network shown

## Slide 5: Thermal Resistance Network
Rcond,o,i in the thermal resistance network shown in figure represents the conduction thermal resistance of each layer.
Rext is the thermal resistance due to the convection/radiative cooling hext on the exposed upper and lower surfaces of the PCB.

## Slide 6: Simplified thermal resistance network for the outer annulus layers
The total equivalent thermal resistance of the thermal resistance network is determined by combining the parallel and series resistances as illustrated
To determine Router Rcond,o,i for each layer is first calculated by determining keff, the average in-plane thermal conductivity of the PCB.
keff is an average of the effective thermal conductivity of each layer, keff,i.

## Slide 7: Effective Thermal conductivity keff,i of Each Layer
The effective thermal conductivity keff,i of each layer is:
where: is the volume fraction of conductor in layer i is the thermal conductivity of the conductor of layer i is the thermal conductivity of the dielectric of layer i
The value of σc,i ranges from 0 to 1.
It can be determined by estimating the conductor coverage area on each layer and dividing that value by the total PCB area (L  W).

## Slide 8: Temperature in ith layer as A Radial Fin
The Bessel equation appears when the Laplace equation is solved in cylindrical coordinates.
The Bessel equation appears for the radial variable in the cylindrical coordinate system.
The equation is named after Friedrich Bessel, a German astronomer.
Bessel first obtained the equation when he was studying star motions.
But the equation first appeared in Daniel Bernoulli's studies of oscillations of a hanging chain.

## Slide 9: Radial Conduction Equation for Each Plane
Define
Radial conduction equation in each plane :
The appropriate boundary conditions:
The equation for the temperature excess becomes

## Slide 10: In-plane Effective Thermal Conductivity
The average in-plane effective thermal conductivity of the entire PCB, keff is:
&
The resistance Router is calculated using the solution for a circular fin expressed as:
where: I0 modified zero order Bessel function of the 1st kind I1 modified zero order Bessel function of the 2nd kind K0 modified first order Bessel function of the 1st kind K1 modified first order Bessel function of the 2nd kind

## Slide 11: Conduction Resistance of Each Outer Layer
With the value of Router known, Rcond,o,i for each layer is calculated using equations:
The equivalent convection coefficient on the periphery of the inner disk for each layer ho,i can now be calculated with equation

## Slide 12: Combining the PCB layer thermal resistances
The next step in the calculation is to determine the value of hb,n, the effective heat transfer coefficient acting on the base of the inner disk of each layer.
This is done by calculating the equivalent heat transfer coefficient that the inner disk of the ith layer applies to the lower surface of the inner disk of the i-1 layer.
This is the heat transfer around the periphery and lower surface to calculate an extended surface with convection hb,i-1.
As and Ps are the cross-sectional area and perimeter respectively of the inner disk.

## Slide 13: Combining the PCB layer thermal resistances
The calculation is started at the last (Nth) layer with hb,N = 0 on the bottom surface of the inner disk for that layer.
hb,N is not set to equal hext since the dissipation of heat from the base of the inner disk will be evaluated separately.

## Slide 14: Iterative Calculation for hb
Using fin equation, hb,N-1 is calculated.
This process is repeated N times for all the layers resulting in an equivalent heat transfer coefficient hb.
This process is illustrated as:
The heat transfer coefficient hb is the equivalent heat transfer coefficient of the conduction resistance due to flow of heat through the inner disk and into the outer annulus of the PCB acting on the heat generating component.

## Slide 15: Thermal resistance network for heat flow through the PCB to the ambient
The conduction thermal resistance due to hb is
R*cond,o includes the thru-plane and in-plane conduction across the PCB.
The “*” notation is used to differentiate this variable from Rcond,o which only accounts for the in-plane conduction in the outer annulus.
The heat flow from the heat generating component through the PCB to the ambient is represented by the thermal resistance diagram

## Slide 16: Thermal resistance network for heat flow through the PCB to the ambient
Flow through the bottom of the inner disk exposed to hext is accounted for with Rcond,inner and Rext,inner thermal resistances.
Rcond,inner is the summation of the thru-plane thermal resistances of each layer, and Rext,inner is the thermal resistance due to hext of the area As.

## Slide 17: Thermal resistance network for heat flow through the PCB to the ambient
The thermal resistances in above figure are combined to a single thermal resistance Rpcb:

## Slide 18: Fraction of Heat Transferred to/thru PCB

## Slide 19: PCB with Thermal Vias
Thermal vias placed under the heat generating component provide a path to more efficiently transfer heat from the heat generating component to the inner layers and base layer of the PCB.
This then allows to the heat to be spread across these layers reducing the thermal resistance of the PCB.

## Slide 20: PCB with Thermal Vias
The analysis of the effect of imbedded thermal vias as shown in above figure requires the calculation of an equivalent through-plane thermal conductivity, kvia,n for the inner disk of each layer.
This is calculated by evaluating the flow of heat through the inner disk of each layer through three parallel thermal resistances

## Slide 21: PCB with Thermal Vias
Three parallel thermal resistances:
Rbarrel, the thermal resistance of the barrel of the thermal via.
Rfiller, the thermal resistance of the filler material of the via if any.
Rmatl,n, the thermal resistance of the layer material surrounding the thermal via in the s s square region

## Slide 22: Case Study : Temperature Estimation POINTS
A cross-section of the power IC mounted to a PCB

## Slide 23: Case Study : Resistance Network

## Slide 24: PCB Thermal Management –Design of Thermal via
Thermal vias should just be part of a larger thermal management strategy for superior thermal management of a PCB.
Placement of thermal vias in a PCB board to aid heat transfer, you should check your placement against your design rules and constraints.
Device-to-board edge thermal resistance of a PCB  20 to 60°C/W)

## Slide 25: PCB Thermal Management – Metal Coins
https://emsxchange.com/pcb-thermal-management-metal-coins/

## Slide 26: Heat Transfer is an Action: Path Function
PCB as a Hot Thermodynamic System
Cold Surroundings