## Slide 1: Thermodynamics of Computing Process
Irreversible Issues in Computation and Electronic Devices
P M V Subbarao
Professor
Mechanical Engineering Department

## Slide 2: Energetic Issues of ICTs
Bennet and Landauer have shown that there exists a minimum amount of energy required to perform any computation.
The ultimate limit on the minimum energy per switching is set at kBT ln2.
It is approximately 10-21J at room temperature, called as the Shannon-von Neumann-Landauer (SNL) limit.
Computing machines inevitably involve devices which perform logical functions that do not have a single-valued inverse.
This logical irreversibility is associated with physical irreversibility.
Generates a minimal heat generation, per machine cycle, typically of the order of kBT for each irreversible function.

## Slide 3: Physical Irreversibility Due to Logical Irreversibility
Bistable potential well.
Consider A
0 and 1 are two equilibrium positions of this well.
Any programing logic to change 0 to 1 is physically interpreted as:

## Slide 4: Energetic Issues of ICTs
This dissipation serves the purpose of standardizing signals and making them independent of their exact logical history.
Even erasing information decreases the overall entropy of the system and this cannot be done without dissipating heat of at least kBT ln2 Joule per bit erased.
Therefore, ideal computation is also thermodynamically irreversible!

## Slide 5: Computational or Information Entropy
For a given value of change in energy of a die (U), there are numerous permutations of bits that yield m ones and (N - m) zeros.
If each of these g(U) permutation states is equally likely, one can define the entropy as
Where g(U) is named as a degeneracy function.
Using simple probability

## Slide 6: Extension of Boltzmann theory :Energy consumption by An Ideal Electronic Device
Ideal electrical work to be consumed for N bits of computation is:
At a room temperature of 298K, Wideal-elec-input = 0.018NeV = N10-21J .
Ideal Electronic Devices can almost work as Adiabatic systems and require no cooling!!!
For a constant volume device:
A closed system executing a process is governed by:
For a solid system:

## Slide 7: Extension of Boltzmann Theory
Ideal electrical work to be consumed for a bit of computation is:
At a room temperature of 298K, Wideal-input = 0.018eV = 10-21J
Why more energy is consumed at higher device temperatures?
Any excess energy must be dissipated and leads to Entropy Generation…

## Slide 8: Physical & Logical Irreversibility
A device logically irreversible if the output of a device does not uniquely define the inputs.
It is believed that devices exhibiting logical irreversibility are essential for computing.
Logical irreversibility in turn implies physical irreversibility, and the latter is accompanied by dissipative effects.

## Slide 9: Fabrication of An Ideal Electronic Device
Ideal electrical work to be consumed for a bit of computation is:
Every thermodynamic process occurs in a material (Device).
Microelectronic devices used as Logic and memory devices
Capacitance is related to a linear dimension, L.
The energy dissipated in the device during charging is:

## Slide 10: Fabrication of An Ideal Electronic Device
Ideal electrical work to be consumed for a bit of computation is:
On the level of elementary operations (e.g. binary switching), the control space is limited by only two parameters – operating voltage and device capacitance.
It is impossible to have zero size device.
If the device (junction) critical geometric dimension, is L, the minimum energy required will be :
L has been from decreased from tenths of micrometers to only a few nanometers.
One immediate implication of scaling is that the actual work decreases as the cube of the device dimensions.

## Slide 11: Dimension of A Junction

## Slide 12: Additional Work to Compute against Thermal Noise
All materials produce noise at a power level proportional to the physical temperature of the material.
The noise is generated by random vibrations of conducting electrons and holes in the material.
This noise is often referred to as thermal noise.
Thermal noise is white and has a Gaussian amplitude distribution.
Thermal noise of a MOSFET with a 0.18-m gate width.
The total Power of thermal noise is:
B is the Device Bandwidth

## Slide 13: Actual Energy consumption by An Irreversible Electronic Device
At a room temperature of 298K, Wideal-input = 0.018eV.
Thermal noise on gates of minimum‐width segments of FET gates leads to channel fluctuations below ~1‐2 eV.
ITRS has minimum gate energy asymptoting to ~2 eV
Also, real logic circuits incur many further overhead factors leading to more losses:
Transistor width 10‐20× min.
Parasitic (junction, etc.) transistor capacitances (~2×)

## Slide 14: Energy consumption by An Irreversible Electronic Device
Multiple (~2) transistors fed by each input to a given logic gate
Fan‐out to a few (~3) logic gates
Parasitic wire capacitance (~2×)
Due to all these overheads, the electrical work input to each bit in real logic circuits is many times larger than the min.‐width gate energy 375‐600× (!) larger.
Practical bit energy for irreversible logic asymptotes to ~1 keV!
Practical, real‐world logic circuit designs can’t just magically cross this ~500× architectural gap!
Thermodynamic limits imply much larger practical limits!

## Slide 15: Evolution of Irreversible Computing

## Slide 16: Second Law of Thermodynamics for Electronic Systems
Heat generation is an unavoidable by-product of operating electronics.
It is impossible to construct an Electric/Electronic System which produces no effect other than the consumption of Electric power from a source and the production of an equivalent amount of ICT Services
It is impossible to develop an electric/electronic device with zero heat generation.
It is difficult to operate electronics at ambient temperature.

## Slide 17: Thermal Management: Designing for Reliability
Device reliability is a complex function of
the heat generated by the operation of an electronic device,
the tools used to dissipate or manage the heat,
the thermal stability of the materials used &
the environment in which the device is required to operate.
Diversity of applications & the increasing demand enjoin diverse thermal management tools.
Popular tools include gap fillers, active cooling systems, heat pipes and heat sinks.

## Slide 18: Holistic Thermal Management Strategies
Reducing the Heat
Removing the Heat
Beating the Heat
Surviving the Environment