## Slide 1: Influence of Cylinder Geometry on Gas to Wall Heat Transfer
P M V Subbarao
Professor
Mechanical Engineering Department
Head, CRDT
Geometry Supports Modest Speed Engines…..

## Slide 2: Evolution of Baby Spark into Baby Flame

## Slide 3: Shape of baby Flame

## Slide 4: Cross-Section of View of Laminar Flame
ri : Initial radius of flame or radius of flame.
rb : instantaneous radius of growing flame.

## Slide 5: Laminar Burning Velocity

## Slide 6
Mixture Burn Time
B
If we take a typical value of 50o crank angle for the overall burn
N (rpm) t90%(ms) Scomb,req (m/s)
Standard car at idle 500 16.7 3.0
Standard car at max power 4,000 2.1 23.8
Formula car at max power 19,000 0.4 125
How is Otto’s Engine Ran at higher Speed????

## Slide 7: Evidence of Organized Structure in an Engine 1200 rpm motored engine
90 Cycle Mean Velocity Distribution
In Mid- Plane
Instantaneous Velocity Distribution
In Mid Plane During Cycle 1
Instantaneous Velocity Distribution
In Mid Plane During Cycle 20

## Slide 8: The Real Growth Kernel to Flame

## Slide 9: Major Steps
Recognition of Turbulence
Design of cylinder for Creation of Turbulence
Characterization of Generated turbulence

## Slide 10: Shapes of Piston Heads

## Slide 11: Shapes of Cylinder Heads

## Slide 12: Creative Ideas to Generate Turbulent Flow : Swirl based systems

## Slide 13: Creative Ideas to Generate Turbulent Flow : Squish based GDI concepts

## Slide 14: Creative Ideas to Generate Turbulent Flow : : Tumble based GDI systems

## Slide 15: Creative Ideas to Generate Turbulent Flow

## Slide 16: Peripheral Technologies
Electronically controlled spray type injector - Hollow cone spray
Tumbling Port
Combustion Chamber Geometry
Hollow Cone Spray
Tumbling Flow
Piston Cavity

## Slide 17
Chart: EFFECT OF PISTON CAVITY ON BSFC
| 2600 | 2750 | 2820 | 2930
No Cavity | 0.85 | 0.81 | 0.79 | 0.77
Cylindical | 0.79 | 0.75 | 0.75 | 0.73
Conical | 0.72 | 0.71 | 0.7 | 0.69
Spherical | 0.73 | 0.69 | 0.71 | 0.7

## Slide 18: Geometrical Characterization of Turbulent Structure
The velocity field in a cylinder contains vortices of sizes (eddies)
  Eddies that are essentially large enough to fill the space available, in our case the engine cylinder,
  Eddies often substantially below a millimeter in size.
The size of the largest eddy can be guessed by asking for the diameter of the largest sphere that will fit in the available space
Hence, at TC the largest eddy will be roughly the clearance height, while at BC it will be roughly the cylinder bore.

## Slide 19: Energetic Characterization of Turbulent Structure
The kinetic energy of these eddies varies:
The largest eddies are relatively weak; as the size drops, the energy rises rapidly to a peak, and then falls continually down to the smallest eddies.
The most energetic eddy, at the peak, which is responsible for most of the transport, is about 1/6 the size of the largest eddy ‐ thus,
1/6 of the bore, or
1/6 of the clearance height

## Slide 20: Engine Geometry Vs Flame Area Maps
The instantaneous area of the spherical flame front the moving across the chamber is one of the main parameter, which is influenced by RBS.
Simulation of flame shape and the interaction between the flame front and the combustion chamber walls demand an advanced geometrical processing algorithms.
In investigations of this type, it is customary to plot maps of normalized flame area (Afl/B2) the normalized flame front radius (Rfl/B).
Influence of RBS on normalized flame area and normalized flame front found to be very significant.

## Slide 21: Flame Shape and Volume in SI Engine

## Slide 22: Classes of Cylinder Geometries
RBS=1.43
RBS=1.0
RBS=0.77

## Slide 23: Flame Area Maps vs RBS
Square Cylinder
RBS=1.0
RBS=1.43

## Slide 24: Flame Area Maps vs RBS
Square Cylinder
RBS=1.0
RBS=0.77

## Slide 25: Comparison of normalized flame areas
RBS0.77
RBS 1.00
RBS01.43

## Slide 26: Wall Wetted Areas
The effect of the stroke-to-bore ratio on combustion, heat transfer and efficiency of a homogeneous charge spark ignition engine of given displacement
Z S Filipi andDNAssanis
W.E. Lay Automotive Laboratory, The University
of Michigan, Ann Arbor, Michigan, USA

## Slide 27: Ability to Transfer Heat : A Signature of Survival
Due to the increased piston- and head surface area, the heat loss increases as the bore/stroke-ratio is increased excessively.
These characteristics favor higher engine speeds, over-square engines are often tuned to develop peak torque at a relatively high speed.
Due to the decreased piston- and head surface area, the heat loss decreases as the bore/stroke-ratio is decreased.
These characteristics favor lower engine speeds and use of poor quality fuels with low running cost.