## Slide 1: Models for Estimation of Gas Temperature in SI Engines
P M V Subbarao
Professor
Mechanical Engineering Department
Head, CRDT
An Essential Requirement to Construct A Sustainable SI Engines…..

## Slide 2: Indicative Gas Cycle of a Four Stroke SI Engine

## Slide 3: Methodology to Development of Artificial Horse
Fuel (Resource)
Land, Water & Air (Sinks)
Automotive Prime Mover
--Cycle
-- Basic Hardware
-- Auxiliaries & Controls
The Great Need :
Mechanical Power

## Slide 4: Cyclic Work To be Delivered by An Artificial Horse
Ideal cycle work to be provided by A Powering Engine:
Air-standard Modelling is the final outcome of 19th century !!!

## Slide 5: Important Feature of Model Vs SI Engine
Fuel/air Ratio
Stoichiometric Mixture
th, %
Lean
Rich
Predictions by Air-standard Cycle
Actual Prime Mover

## Slide 6
Otto’s Hardware Model for Artificial Horse
A
I
R
Intake
Stroke
FUEL
Ignition
Power
Stroke
Fuel/Air
Mixture
Compression
Stroke
Combustion
Products
Exhaust
Stroke
Actual
Engine Cycle

## Slide 7
Otto’s Hardware Model for Artificial Horse
A
I
R
Intake
Stroke
FUEL
Ignition
Power
Stroke
Fuel/Air
Mixture
Compression
Stroke
Combustion
Products
Exhaust
Stroke
Air
Compression
Process
TC
Qin
Const volume
heat addition
Process
Expansion
Process
Actual
Engine Cycle
Thermodynamic Model
Cycle
Qout
BC
Const volume
heat rejection
Process

## Slide 8: Otto’s Model Cycle for his Artificial Horse
Process 1 2 Isentropic compression
Process 2  3 Constant volume heat addition
Process 3  4 Isentropic expansion
Process 4  1 Constant volume heat rejection

## Slide 9: Engine Geometry Vs Air standard Otto Cycle
The term stoichiometry was first used by Jeremias Benjamin Richter in 1792 : the Art of Measuring the Chemical Elements.
The term is derived from the Ancient Greek words στοιχεῖον stoicheion "element" and μέτρον metron "measure".

## Slide 10: Advanced Analysis Missed in 20th Century : AS Otto Cycle Volume to meet the Demand

## Slide 11: Cycle Volume Vs Cylinder Volume
A given cycle can be met using m number of similar cylinders if required.
Any restriction on stroke length can be satisfied by using multi-cylinder engine.
Why was Geometric-Chemical analysis ignored in 20th Century and before?

## Slide 12: Indicative Gas Cycle of a Four Stroke SI Engine
A
I
R
Intake
Stroke
FUEL
Combustion
Products
Exhaust
Stroke
Ignition
Power
Stroke
Fuel/Air
Mixture
Compression
Stroke

## Slide 13: Modelling of Intake Process : SI Engine
A
I
R
FUEL
SI Engine

## Slide 14: Instantaneous Heat Transfer During Intake Process

## Slide 15: Total Mass of mixture inhaled during Intake Process
A
I
R
FUEL

## Slide 16
Modeling of Exhaust Process : SI Engine
Combustion
Products
Exhaust
Stroke

## Slide 18: 21st Century Phenomenological Models for Engine Cycles
Fuel-air analysis is more accurate analysis when compared to Air-standard cycle analysis.
An accurate representation of constituents of working fluid is considered.
More accurate models are used for properties of each constituents.
Process | Otto’s Engine | Diesel’sEngine
Intake | Air + Fuel +Residual gas | Air + Residual gas
Compression | Air+Fuel vapour +Residual gas | Air + Residual gas
Expansion | Combustion products | Combustion Products
Exhaust | Combustion products | Combustion Products

## Slide 19: Fuel-Air Model for Otto Cycle
Otto
Cycle
Air+Fuel vapour +Residual gas
TC
BC
Compression
Process
Const volume
combustion
Process
Expansion
Process
Const volume
Blow down
Process
Products of Combustin
Products of Combustin

## Slide 20: 21st Century Analysis of Ideal Otto Cycle
This is known as Fuel-air Cycle.
1—2 Isentropic compression of a mixture of air, fuel vapour and residual gas without change in chemical composition.
2—3 Complete combustion at constant volume, without heat loss, with burned gases in chemical equilibrium.
3—4 Isentropic expansion of the burned gases which remain in chemical equilibrium.
4—5 Ideal adiabatic blow down.

## Slide 21: Isentropic Compression Process: 1 - 2
For a infinitesimal compression process:
Mass averaged properties for an ideal gas mixture:
Assume ideal gas nature with variable properties:

## Slide 22: Variation of Specific Heat of Ideal Gases
Gas | C0 | C1 | C2 | C3
Air | 1.05 | -0.365 | 0.85 | -0.39
Methane | 1.2 | 3.25 | 0.75 | -0.71
CO2 | 0.45 | 1.67 | -1.27 | 0.39
Steam | 1.79 | 0.107 | 0.586 | -0.20
O2 | 0.88 | -0.0001 | 0.54 | -0.33
N2 | 1.11 | -0.48 | 0.96 | -0.42

## Slide 23
g
cp
cv

## Slide 24
Properties of Fuels
Fuel | C0 | C1 | C2 | C3 | C4
Methane | -0.29149 | 26.327 | -10.610 | 1.5656 | 0.16573
Propane | -1.4867 | 74.339 | -39.065 | 8.0543 | 0.01219
Isooctane | -0.55313 | 181.62 | -97.787 | 20.402 | -0.03095
Gasoline | -24.078 | 256.63 | -201.68 | 64.750 | 0.5808
Diesel | -9.1063 | 246.97 | -143.74 | 32.329 | 0.0518

## Slide 25: Isentropic Compression model with variable properties : 1 - 2

## Slide 26: True Phenomenological Model for Isentropic Compression
Let the mixture is modeled as:

## Slide 27: Carnot’s Concept of Air-Standard Model
Let the mixture is modeled as air with constant properties measured at STP:

## Slide 28: Realistic Estimate of Work for Isentropic Compression
Let the mixture is modeled as:

## Slide 29: Generalized First Order Models for Variable Specific Heats
ap = 28.182 – 32.182 kJ/kmol.K
bv = 19.868 – 23.868 kJ/kmol.K
k1 = 0.003844–0.009844 kJ/kmol.K2
For design analysis of Engine Models:

## Slide 30: The Role of Isentropic Compression
Second order Property Model:
First order Property Model:
Ready for combustion:
In a combustion reaction, bonds are being broken and formed between different atoms in molecules.
The parts of the molecules that undergo bond breakage and formation need to line up with each other.
There needs to be the appropriate overlap in the orbitals that are "donating" and "accepting" electrons.
The probability of occurrence of appropriate overlap is proportional to temperature of reacting molecules.

## Slide 31: Collision Theory
Collision theory says that ”in order for a chemical reaction to happen, three separate things need to happen” :
1. The molecules have to hit each other
2. The molecules have to hit each other in the right way (both have to be facing the right way)
3. The molecules have to hit each other with enough speed (energy of motion, or "kinetic energy") to activate the reaction.
Number of successful collisions  Frequency of collisions  Time available for collision.

## Slide 32: Phenomenological Modeling of Combustion
Engineering Objective of Combustion:
To Create Maximum Possible Temperature through conversion of free energy into microscopic kinetic energy.
Thermodynamic Strategy for conversion:
Constant temperature combustion
Constant volume combustion
Constant pressure combustion

## Slide 33: Engineering Strategy to Utilize A Resource
Engineering constraint: Both combustion and expansion have to be finished in a single stroke.
Rapid combustion : Constant Volume combustion
  Less time to combustion process.
  More time to adiabatic expansion
Slow combustion : Constant pressure combustion
  More time to combustion process.
  Less time to adiabatic expansion

## Slide 34: 2—3 Complete combustion at constant volume, without heat loss.
2—3 : Loss of Purity of Substance
Otto’s Strategy : Premixed, Homogeneous Combustion

## Slide 35: Second law limit on possible extent of reaction
Reactants Products
At any time a reactor contains a combination of reactants and products.
A reaction is said to be complete when the entropy of an adiabatic reactor reaches its maximum value.
The value of maximum entropy will vary with the pressure and temperature of the reaction.
A reaction system and parameters of reaction should be designed such that the maximum entropy is obtained when the reaction is almost complete (>98%).

## Slide 36
Mathematical Model for Culmination of Reaction
For every fuel, a designer should know all possible reactants !!!
Some products will influence the efficiency of reaction.
Few other may not influence the efficiency of reaction but severely affect the environment.
The optimal parameters for efficient reaction may not be optimal for safe reaction !!
There may be a need to use secondary reactor with catalysts.
Catalytic Converter

## Slide 37: Stoichiometry of Actual Combustion
CXHYSZOK +e 4.76 (X+Y/4+Z-K/2) AIR → P CO2 +Q H2O +R SO2 + T N2 + U O2 + V CO+WCH4
Conservation species:
Conservation of Carbon: X = P+V+W
Conservation of Hydrogen: Y = 2 Q4W
Conservation of Oxygen : K + 2 e (X+Y/4+Z-K/2) = 2P +Q +2R +2U+V
Conservation of Nitrogen: 2 e 3.76 (X+Y/4+Z-K/2) = T
Conservation of Sulfur: Z = R

## Slide 38: Modeling of Combustion
CXHYSZ +e 4.76 (X+Y/4+Z) AIR + Moisture in Air + Moisture in fuel → P CO2 +Q H2O +R SO2 + T N2 + U O2 + V CO+WCH4
Exhaust gases: P CO2 +QH2O+R SO2 + T N2 + U O2 + V CO+WCH4 kmols.
Excess air coefficient : e.
Volume fraction = mole fraction.
Volume fraction of CO2 : x1 = P * 100 /(P+Q+R + T + U + V+W)
Volume fraction of CO : x2= VCO * 100 /(P +Q+R + T + U + V+W)
Volume fraction of O2 : x4= U * 100 /(P +Q+R + T + U + V+W)
Volume fraction of N2 : x5= T * 100 /(P +Q+R + T + U + V+W)

## Slide 39: 2—3 Complete & Adiabatic combustion at constant volume
0
0
First law for a Closed system under going process 2 - 3

## Slide 40: Engineering Model for Prediction of Highest Temperature
Second order Property Model:
First order Property Model:

## Slide 41: 2—3 constant volume Heat addition to air with constant properties
0
First law for a Closed system under going process 2 - 3

## Slide 42: 3—4 Isentropic expansion of the burned gases
For a infinitesimal expansion process:
Mass averaged properties:
Using second order models for properties:

## Slide 43: 3—4 Isentropic expansion of Standard Air
For a infinitesimal expansion process:

## Slide 44: Limitation of Four Bar Mechanism & Scavenging
Expansion Ratio = Compression Ratio.
In a Real engines of 19th & 20th Century:
Expansion Ratio < Compression Ratio?
21st Century Engines:
Expansion Ratio > Compression Ratio.

## Slide 45: The Quick Closure Model

## Slide 46: Air-standard Otto Cycle & Clue to Achieve Higher Efficiency

## Slide 47: Hardware Feasibility of Otto Cycle
Net cycle work:
Piston Displacement volume
Work done per unit piston displacement volume:

## Slide 48: Thermo-chemical Feasibility of Otto’s Model

## Slide 49: Thermo-chemical Feasibility of Ignition
Saturation line
Lower Flame Limit
Upper Flame Limit
Onset of
Piloted Ignition Region
Vapour Pressure in Air
Mixture Temperature

## Slide 50: Design Constraints: Flammability Characteristics
Mixture Temperature
Stoichiometric Line
Flammable Vapour
Lean Mixture Line
Rich Mixture
Flammable mist
Flash Point
Burning Impossible

## Slide 51: Irrationality of Otto’s Model
Typical SI engines
9 < r < 11
k = 1.4
Fuel/Air
Mixture
Compression
Stroke

## Slide 52: Flame Quenching at Wall

## Slide 53: Live with A Promising Irrational Engine Model????
Artificial Horses
Advanced Cities
Generation of
photochemical smog
eye and respiratory irritation in humans
epinasty, chlorosis, curling, leaf abscission and growth retardation in plans

## Slide 54
Engine Damage From Severe Knock
Damage to the engine is caused by a combination of high temperature and high pressure.
Piston
Piston crown
Cylinder head gasket
Aluminum cylinder head

## Slide 55: Critical Compression Ratio
Formula Name Critical r
CH4 Methane 12.6
C3H8 Propane 12.2