## Slide 1: Eco-friendly Cycles for Automotive Prime Movers
P M V Subbarao
Professor
Mechanical Engineering Department
Broadening of Expansion Process ….

## Slide 2: Actual Thermodynamic Cycle & Incomplete Execution of Expansion

## Slide 3: P-V diagram of 4-stroke cycle : SI Engine with Natural Aspiration : 4000rpm

## Slide 4: The Crisis
The problem is due to the fact, that the single reciprocating device has a compression stroke which is equal to the expansion stroke.
On one hand, you need a high expansion stroke in order to convert the maximum of thermal energy into work.
On the other hand, you need a rather low compression stroke, in order to limit the thermal and mechanical stresses, as well as the uncontrolled ignition for gasoline cycles.

## Slide 5: The Unreasonable Bias : CM vs CV
A
I
R
Combustion
Products
Ignition
Intake
Stroke
FUEL
Fuel/Air
Mixture
Compression
Stroke
Power
Stroke
Exhaust
Stroke

## Slide 6: A Pair of Cylinders for Expansion
Fuel resources and Ecology are valuable.
Valuable resources must be used in a comprehensive/elaborative way.
The high-pressure cylinder: Main duty: Clean Combustion
The low-pressure cylinder: Main Duty: Complete Expansion

## Slide 7: In 2000, a new engine is born ...
Three cylinder 5-Stroke engine
Five Stroke Internal Combustion Engine : A new concept for internal combustion engines, by Gerhard Schmitz, St.Vith 2011, Belgium

## Slide 8: The Five Stroke Cycle
The five-stroke cycle consists in the following steps:
1. Intake process in the high pressure (HP) cylinder
2. Compression, followed by the ignition in HP cylinder
3. First expansion of the burned gases in HP Cylinder
4. Second expansion of the burned gases in HP+LP cylinders
5. Exhausting of the burned gases by LP Cylinder

## Slide 9: Basic Module of Modular Engine
Two HP Cylinders.
One HP Cylinder
Three valves
Two five stroke Cycles in two crank revolutions.
Fresh air Intake
Fuel injector
Expansion ratio > Compression ratio.

## Slide 10: Onset of Intake Process in HP-1 Cylinder
Rate of air-fuel mixture into HP Cylinder 1,

## Slide 11: Intake Process in HP-1 Cylinder: Start to End
Start
End

## Slide 12: Onset of Compression in HP-1Cylinder
Compression in HP -1

## Slide 13: Compression Process in HP-1 Cylinder
Start
End
Ignition in HP 1

## Slide 14: Onset of Combustion and Partial Expansion in HP-1 Cylinder
Combustion + Expansion in HP 1

## Slide 15: Combustion and Partial Expansion in HP-1 Cylinder
Start
End

## Slide 16: Onset of Second Part of Expansion in LP Cylinder
Gas Transfer from HP 1
Extended Expansion with LP Cylinder

## Slide 17: Second Part of Expansion in HP-1+LP
Start
End

## Slide 18: Exhaust Process in LP Cylinder
Exhaust Process in LP Cylinder,
Opening of Exhaust valve & onset of
Exhaust process in LP Cylinder
Simultaneous occurrence of Intake Process in HP-1

## Slide 19: Exhaust Process in L P Cylinder
Start
End

## Slide 20: Onset of Second Cycle in HP-2
Combustion + Expansion in HP 1
Intake in HP2
Exhaust from LP

## Slide 21: Intake process in HP-2
Start
End
Exhaust Process by LP and First Expansion in HP-1

## Slide 22: Onset of Compression in HP-2
Gas Transfer from HP 1
Compression in HP 2
Onset of Extended Expansion in LP

## Slide 23: Compression & Igntion Process in HP-2
Start
End

## Slide 24: Combustion and Expansion in Process in H P-2 Cylinder
Start
End

## Slide 25: Transfer from HP-2 to LP & Extended Expansion
Compression in HP -1
Transfer Hp Cylinder 2
Extended Expansion in LP Cylinder

## Slide 26: Combined Expansion in HP-2 & LP Cylinders
Start
End

## Slide 27: Extended Pressure vs Crank Angle Diagram

## Slide 28: Work Delivered during Expansion in LP Cylinder : Twice in a Cycle

## Slide 29: The Five Stroke Cycle
The five-stroke cycle consists in the following steps:
1. Admission in the high pressure (HP) cylinder
2. Compression, followed by the ignition
3. First expansion of the burned gases
4. Second expansion of the burned gases
5. Exhausting of the burned gases.