## Slide 1: Green Methods for Eco-friendly Combustion in CI Engines
P M V Subbarao
Professor
Mechanical Engineering Department
Add Homogenization to Heterogeneous Combustion Process….

## Slide 2: Need to Care the Heterogeneous Combustion in more detail
Ecology is sensitive to Diesel emissions.
Efficient utilization of energy resources
The conventional diffusion combustion can not meet upcoming stringent emission norms (Higher Smoke and NOx emissions )
Banning of Diesel engines across various Cities world wide regardless of their high efficiency and power out put (e.g. Delhi, Chandigarh)
Emerging topic worldwide to keep the High efficient diesel fuelled vehicles rolling on the roads.
Demands a thorough modification of Turbulent Non-premised Flames.

## Slide 3: Temporal Evolution of Spatial Distribution of Equivalence Ratio in CI Engines
rcylinder

## Slide 4: Rich Equivalence Ration & Onset of Premixed Ignition-Combustion
Fuel Equivalence Ratio

## Slide 5: Auto Ignition & Premixed Burning
Fuel rich pre-premixed burning
– Release of energy and release of Chemiluminescence emissions.

## Slide 6: Transition into Diffusion Burning

## Slide 7: Diffusion Burning Flame
Oxidation of incomplete products of the rich premixed combustion.
Fuel vapor at the ‘jet’/ air interface
Local Extinction

## Slide 8: Diesel Engineer with Eco-inimical Combustion

## Slide 9
Diesel Engine Menace
Stratified charge and unacceptable occurrence of φ-T combination in cylinder.
Stoichiometric zones: High AFT-NOx in post flame.
Rich zone: High PAH- Soot.
Lean zone: Poor combustion- High CO and UBHC
Why Menace?

## Slide 10: First Generation Common Rail Diesel Injection System
The Common Rail Diesel Injection System delivers a more controlled quantity of atomized fuel.
This leads to better fuel economy; a reduction in exhaust emissions; and a significant decrease in engine noise during operation.

## Slide 11: History of CRDI
The common rail system prototype was developed in the 1960's by Robert Huber of Switzerland.
The technology was further developed by Dr.Marco Ganser at the swiss Federal Institute of Technology in Zurich.
The first successful usage in production vehicle began in Japan in the mid-1990's by Dr.Shohei Itoh & Masahina Miyaki of the Denso Corporation.

## Slide 12: Present Generation (Electronically Controlled) CRDI

## Slide 13: Common Rail Diesel injection system
In the Common Rail system, an accumulator, or rail, is used to maintain a common reservoir of fuel under a consistent controlled pressure that is isolated from the fuel injection locations.
A high-pressure pump increases the fuel pressure in the accumulator up to 1,600 bar .
The pressure is set by the engine control unit and is independent of the engine speed and quantity of fuel being injected into any of the cylinders.
The fuel is then transferred through rigid pipes to the fuel injectors, which inject the correct amount of fuel into the combustion chambers.

## Slide 14: Eco-friendly Equivalence Ratio for CI Combustion
Perfect CI Engine
Low Pressure Injection
CRDI

## Slide 15: Modern Injectors for CRDI
The injectors used in Common Rail systems are triggered externally by an Electronic Diesel Control, (EDC) unit.
EDC controls all the engine injection parameters including the pressure in the fuel rail and the timing and duration of injection.
Some common rail injectors are controlled by a magnetic solenoid on the injector.
In some injectors, hydraulic force from the pressure in the system is used to open and close the injector, but the available pressure is controlled by the solenoid triggered by the Electronic Diesel Control unit.

## Slide 16: Next Generation Injectors for CRDI
Some new injectors use Piezo crystal wafers to actuate the injectors.
These crystals expand rapidly when connected to an electric field.
In a Piezo inline injector, the actuator is built into the injector body very close to the jet needle and uses no mechanical parts to switch injector needles.
The electronic diesel control unit precisely meters the amount of fuel injected, and improves atomization of the fuel by controlling the injector pulsations.
This results in quieter, more fuel-efficient engines; cleaner operation; and more power output.

## Slide 17: Next Generation Diesel Injection Systems
The HEUI (Hydraulically Actuated Electronically Controlled Unit Injector) technology

## Slide 18: Eco-friendly Equivalence Ratio for CI Combustion

## Slide 19
The Holistic Combustion Method
Fuel & Air Charge Undergoes Compression
Spontaneous Reaction Throughout Cylinder
Low Temperature and Fast Reaction Gives Low NOx

## Slide 20: Mildly Knocking Eco-friendly Engine

## Slide 21: Homogeneous Charged Combustion
To achieve the kind of combustion depicted in previous discussion;
Three major aspects should be addressed:
1. How to create a homogeneous mixture in a CI engine?
2. How to achieve self ignition of this mixture?
3. How to control combustion so that engine is safe and performance is better?

## Slide 22: Effect of mixing time on Early (pilot) injection on combustion process

## Slide 23: Advanced CI Engine for Next Decade
HCCI-DI Engine.
Divide the fuel into Primary (main) and Pilot (Early) Fuel.
Pilot fuel is responsible for homogenization.
Primary fuel is responsible for Compression Ignition.
Identify the conditions for avoidance of Self Ignition due to Pilot fuel Injection.
How to develop a dual injection system????

## Slide 24: Developed HCCI-DI fuel injection system
External pump (Pilot)
2 pumps
Belt drive from extended
cam shaft
Fuel injector
HP pipe 1, 2 and 3
T-junction
Split ratio control lever
Inj. timing control cam
Developed System
Multi injection using single Injector without any geometry modification

## Slide 25: Schematic Diagram of HCCI-DI Engine test setup
Engine specifications

## Slide 26: Dual Injection HCCI Engines

## Slide 27: Temporal Evolution of Spatial Distribution of Equivalence Ratio during Pilot Injection
0.
0.
0.
0.
0.
0.
0.
rcylinder

## Slide 28: Temporal Evolution of Spatial Distribution of Equivalence Ratio during main injection
rcylinder
0.0
0.4
0.8
1.2
1.6
2.0
2.4

## Slide 29: Eco-friendly Equivalence Ratio for CI Combustion

## Slide 30: Diagnostic Testing of HCCI-DI Engine

## Slide 31: Rate of Combustion (Heat Release rate) in a Diesel Engine

## Slide 32: In-cylinder Processes in a Mild HCCI Engine

## Slide 33: Pace of Combustion in a Mild HCCI-DI Engine

## Slide 34: Diagnostic Testing of HCCI-DI Engine

## Slide 35: In-cylinder Processes in a Harsh HCCI-DI Engine

## Slide 36: In-cylinder Processes in a Pure HCCI-DI Engine

## Slide 37: Effect of Split Ratio on Range of Equivalence Ratio in CI Engines

1.0
3.0
5.0
7.0
Lean Mixture Zone
Rich Mixture Zone

## Slide 38: Effect of Split Ratio on Range of Equivalence Ratio in CI Engines

1.0
3.0
5.0
7.0
Lean Mixture Zone
Rich Mixture Zone

## Slide 39: Effect of Split Ratio 80 % (Harsh) HCCI DI Engine Cylinder Process

## Slide 40: Fuel Economy of Homogenization
Chart: Split ratio
| 0 | 0.2 | 0.4 | 0.60000000000000064 | 0.8
HCCI-DI | 243.7133 | 235.7595 | 234.1901 | 233.33 | 224.2608

## Slide 41: Eco-friendly Behaviour of Homogenization
Chart: Split ratio (-)
| 0 | 0.2 | 0.4 | 0.60000000000000064 | 0.8
HCCI-DI | 28.3 | 23.9 | 18.2 | 14.82 | 10.2
Smoke Opacity is the fraction (or %) of incident light which is adsorbed or scattered by the particulate matter in exhaust gas.

## Slide 42: Control of Particulates in 80 % (Harsh) HCCI DI Engine - 1
Chart: Main injection timing (ºCA BTDC)
| 26
Baseline | 23.7
HCCI-DI | 7.9 | 9.2 | 10.6 | 14.82 | 17.2

## Slide 43: Control of Particulates in 80 % (Harsh) HCCI DI Engine - 2
Chart: Pilot injection timing (ºCA BTDC)
| 270 | 180 | 90 | 45
HCCI-DI | 6.8 | 10.6 | 17.82 | 21.2

## Slide 44: Effect of Degree of Homogenization : Particulates
Chart: Split ratio (-)
| 0 | 0.2 | 0.4 | 0.60000000000000064 | 0.8
HCCI-DI | 28.3 | 23.9 | 18.2 | 14.82 | 10.2

## Slide 45: Effect of Degree of Homogenization : HC Emissions
Chart: Split ratio
| 0 | 0.2 | 0.4 | 0.60000000000000064 | 0.8
HCCI-DI | 0.1619 | 0.26518 | 0.58403 | 0.83894 | 1.1567

## Slide 46: Effect of Degree of Homogenization : CO Emissions
Chart: Split ratio (-)
| 0 | 0.2 | 0.4 | 0.60000000000000064 | 0.8
HCCI-DI | 2.6175 | 5.3591 | 9.4421 | 11.6925 | 13.0471

## Slide 47: Effect of Degree of Homogenization : NOx Emissions
Chart: Split ratio (-)
| 0 | 0.2 | 0.4 | 0.60000000000000064 | 0.8
HCCI-DI | 8.0018 | 6.392 | 6.8191 | 8.3676 | 9.3156

## Slide 48: Schematic Diagram of HCCI-DI Engine test setup with EGR & Fuel Heating

## Slide 49: Effect of Exhaust Gas recirculation
Chart: EGR (%)
| 0 | 10 | 20 | 30
HCCI-DI | 1.1567 | 1.6085 | 2.2139 | 2.7652
Chart: EGR (%)
| 0 | 10 | 20 | 30
HCCI-DI | 9.3156 | 7.157 | 4.218 | 2.7127
Chart: EGR (%)
| 0
Baseline | 24.2
HCCI-DI | 10.2 | 10.8 | 12.2 | 16.4
Chart: EGR (%)
| 0
Baseline | 1.6275
HCCI-DI | 13.0471 | 14.0113 | 15.4875 | 17.2402

## Slide 50: Role of Fuel Heating
Chart: Fuel temperature (ºC)
| 40 | 60 | 80 | 100 | 120
HCCI-DI | 16.3462 | 16.99 | 17.0241 | 16.1128 | 16.2926
Chart: Fuel temperature (ºC)
| 40 | 60 | 80 | 100 | 120
HCCI-DI | 1.8873 | 1.8994 | 1.8408 | 1.7173 | 1.6124
Chart: Fuel temperature (ºC)
| 40 | 60 | 80 | 100 | 120
HCCI-DI | 14.4 | 14.2 | 13.4 | 12.2 | 10.4
Chart: Fuel temperature (ºC)
| 40 | 60 | 80 | 100 | 120
HCCI-DI | 0.87447 | 0.95022 | 1.0246 | 1.0375 | 1.296
Chart: Fuel temperature (ºC)
| 40 | 60 | 80 | 100 | 120
HCCI-DI | 242.5392 | 240.8625 | 236.6981 | 231.8689 | 225.0618

## Slide 51: High Speed Operation of HCCI-DI Engine
Chart: Engine speed (rev/min)
| 1600 | 1800 | 2000 | 2200 | 2400 | 2600
5 bar IMEP | 73 | 94 | 98 | 110 | 160 | 194
No load | 32 | 29 | 53 | 64 | 73 | 87
Chart: Engine speed (rev/min)
| 1600 | 1800 | 2000 | 2200 | 2400 | 2600
5 bar IMEP | 16.2365 | 18.9865 | 22.0364 | 25 | 29 | 31
No load | 5.896 | 4.0231 | 7.569 | 7 | 9 | 11
Chart: Engine speed (rev/min)
| 1600 | 1800 | 2000 | 2200 | 2400 | 2600
5 bar IMEP | 130 | 173 | 256 | 332 | 452 | 572
No load | 113 | 152 | 213 | 269 | 311 | 368
Chart: Engine speed (rev/min)
| 1600 | 1800 | 2000 | 2200 | 2400 | 2600
5 bar IMEP | 0.149 | 0.303 | 0.5898 | 0.79 | 0.96 | 1.4
No load | 0.13 | 0.28 | 0.42061 | 0.61 | 0.72 | 0.92

## Slide 52: Special Parameters for Combustion Characterization
Identification of Different Combustion Parameters