## Slide 1: Free Religion Compression Ignition Engines
P M V Subbarao
Professor
Mechanical Engineering Department
I I T Delhi
Eco-friendly Combustion in CI engines…..

## Slide 2
Religious I.C. Engines

## Slide 3
CI Religion in I.C. Engines
Diesel Engines
 High CR
 No throttling , quality governed,
High fuel economy at part load
Best suited for low SIT fuels
Very good & faster reacting fuels
Low HC emissions
Low specific power
Heterogeneous combustion
High NOx and PM (Smoke)

## Slide 4
SI Religion in I.C. Engines
MPFI Engines
High Specific Power
Homogeneous combustion
Very Low PM & low Nox
Best suited for High SIT Fuels
Very good for slow reacting fuels
High HC emissions
Poor performance at part load

## Slide 5
BEST Qualities of Two Religions in I.C. Engines
The Free Religious Engine
High power at full load  High CR, high vol.
High Fuel economy  Distinctly stratified charge,
Quality governing
Lower HC, PM & NOx.

## Slide 6
BEST Qualities of Two Religions in I.C. Engines
Why SI Engine needs to be Homogeneous mixture only?
Why can not CI Engine use Homogeneous mixture?
Religious Philosophy:
SI Engine – Homogeneous Mixture – Light Fuels
CI Engine – Heterogeneous Mixture – Heavy Fuels

## Slide 7: First Level of Free Religion CI Engine for Next Decade
HCCI-DI Engine.
Divide the fuel into Primary (main) and Pilot (Early) Fuel.
Pilot fuel is injected during late intake to early compression and responsible for homogenization.
Primary fuel is responsible for Compression Ignition and injected during later compression.
Split Ratio is the ratio of pilot fuel to total fuel.
Identify the conditions for avoidance of Self Ignition due to Pilot fuel Injection.
Develop a dual injection system.

## Slide 8: Fuel Economy of Homogenization
Chart: Split ratio
| 0 | 0.2 | 0.4 | 0.60000000000000064 | 0.8
HCCI-DI | 243.7133 | 235.7595 | 234.1901 | 233.33 | 224.2608

## Slide 9: Eco-friendly Behaviour of Homogenization
Chart: Split ratio (-)
| 0 | 0.2 | 0.4 | 0.60000000000000064 | 0.8
HCCI-DI | 28.3 | 23.9 | 18.2 | 14.82 | 10.2
Smoke Opacity is the fraction (or %) of incident light which is adsorbed or scattered by the particulate matter in exhaust gas.

## Slide 10: Effect of Degree of Homogenization : HC Emissions
Chart: Split ratio
| 0 | 0.2 | 0.4 | 0.60000000000000064 | 0.8
HCCI-DI | 0.1619 | 0.26518 | 0.58403 | 0.83894 | 1.1567

## Slide 11: Effect of Degree of Homogenization : CO Emissions
Chart: Split ratio (-)
| 0 | 0.2 | 0.4 | 0.60000000000000064 | 0.8
HCCI-DI | 2.6175 | 5.3591 | 9.4421 | 11.6925 | 13.0471

## Slide 12: Effect of Exhaust Gas recirculation
Chart: EGR (%)
| 0 | 10 | 20 | 30
HCCI-DI | 9.3156 | 7.157 | 4.218 | 2.7127

## Slide 13: Field Acceptability Testing of HCCI-DI Engine

## Slide 14: In-cylinder Processes in a Harsh HCCI-DI Engine

## Slide 15: In-cylinder Processes in a Pure HCCI-DI Engine

## Slide 16: Special Parameters for Combustion Characterization
Identification of Different Combustion Parameters

## Slide 17: Evolution of CI Engine from Polite to Aggressive Attitude

## Slide 18: Belligerent Nature of HCCI Engine
Chart: 
| 0
Baseline | 62.4337
HCCI-DI | 55.0244 | 55.7065 | 57.1656 | 61.6834 | 64.8244
Chart: 
| 0
Baseline | 5.5
HCCI-DI | 6.5 | 7 | 7 | 6.5 | 5

## Slide 19: Evolution of Onset of Combustion
Chart: 
| 0
Baseline | 10
HCCI-DI | 7 | 8 | 9.5 | 10.5 | 12

## Slide 20: Selection of PIT : For Safe Combustion: 80% HCCI

## Slide 21: Selection of PIT : For Safe Combustion

## Slide 22: Evolution of CI Engine from Polite to Aggressive Attitude in HCCI Mode
There is a need to control rate of combustion reaction in HCCI.

## Slide 23: Secular Classification of Fuels
All available fuels are classified based on Reactivity, namely low reactivity fuels and High reactivity fuels.
Low Reactivity fuels: High Octane number or low cetane number.
LRF: Fossil fuels: CNG, Gasoline etc.
LRF Renewable fuels: Bio-gas, ethanol, methanol etc.
High Reactivity fuels: Low Octane number or High Cetane number.
HRF Fossil fuels: Diesel and other heavy fuel oils.
HRF Renewable fuels: Non edible vegetable oils, Bio-Diesel…

## Slide 24: Definition of A Secular Engine
A method of creating a partially premix and partially stratified in-cylinder mixture with fuels of opposing cetane rating or reactivity, is basis for development of a secular engine.
Compression Ignition facilitates high compression ratio.
Therefore, a secular engine named as Reactivity Controlled Compression Ignition Engine (RCCI engine) is an ultimate option.
The auto-ignition is initiated by the high cetane rating fuel spray into the low cetane rating fuel-air mixture.
The resulting cetane rating gradient creates varying control (resistances) to onset of subsequent ignition and progress of combustion.

## Slide 25
Engine specifications | 
Bore × Stroke (mm) | 116×102
Connecting rod (mm) | 230
Displacement (cc) | 950
No. of valves | 2
Exhaust valve open | 35.5⁰ CA bBDC
Exhaust valve close | 4.5⁰ CA aTDC
Intake valve open | 4.5⁰ CA bTDC
Intake valve close | 35.5⁰ CA aBDC
Max. power (rated) | 10HP @ 1500 rpm
Max. power (de-rated) | 7 HP @ 1500 rpm
Compression ratio | 16 (rated 17.5)
Injection timing (⁰CA bTDC) | 20
Injection pressure (bar) | 200
The Engine

## Slide 26
Schematic layout of RCCI Engine Test Rig

## Slide 27
Photographic view of the overall experimental set up

## Slide 28
Close photographic view of the engine PFI, DI, head and sensor mounting spot

## Slide 29
Engine Test Rig & List of Direct Measurements

## Slide 30
Estimated Input Parameters : Degree of Homogeneity
Energy Share (%)

## Slide 31
Estimated Input Parameters : Degree of Reactivity
Mixture Cetane Number
The mixture cetane rating (CNmix) is the effective in-cylinder cetane rating due to contributions from both low and high cetane rating fuels

## Slide 32
Estimated Performance Parameters : Combustion efficiency

## Slide 33
Estimated Performance Parameters : Emissions
Volumetric emissions were converted into g/kWh based on the flow rates and molecular weight considerations.
Conversion of smoke % to g/kWh involved a curve fitting by conversion of measured smoke % to the filter smoke number (FSN) by an empirical formula.
FSN then converted into particulate volume fraction.

## Slide 34: Selection of Optimal Operational Parameters

## Slide 35
Optimal Selection of Main Fuel Injection Timing
Diesel-Gasoline RCCI

## Slide 36
Control of Soot
Diesel-Gasoline RCCI

## Slide 37
Control of NOx
Diesel-Gasoline RCCI

## Slide 38
Optimal Selection of Main Fuel Injection Timing
Diesel-Enriched Biogas RCCI

## Slide 39
Control of Particulates
Diesel-Enriched Biogas RCCI

## Slide 40
Control of NOx
Diesel-E-Biogas RCCI

## Slide 41
Polite Nature of RCCI Engine