## Slide 1: The Green Hybrid Prime Movers
P M V Subbarao
Professor
Mechanical Engineering Department
An Attempt to Use A Pair of Most reversible and Zero Carbon Footprint Prime Movers.....

## Slide 2: Future Conceptual Hybrid Scheme
High Energy density energy source
Digestive Prime Mover
Low Energy density energy source
Tractive Prime Mover
Conventional: Electric Battery
Unconventional: Hydraulic storage
Conventional: CI & SI I C Engines
Unconventional: Fuel Cells
Conventional: Electric MGs
Unconventional: Hydraulic MGs
Conventional: Fossil Fuels
Unconventional: Green Fuels

## Slide 3: Reversible Process/Reactions are Green
An electro-chemical reactions is more reversible than combustion.
All fuel resources available for transportation must be converted into green fuel.
A green fuel participates in most reversible reaction/process in a specific hardware system.
Out of know fuels Hydrogen can perform most efficient reversible reaction to release calorific value directly as electric energy.
These systems are known as Fuel Cell.
A Fuel Cell carries out inverse process of an electrolyzer.

## Slide 4: Green Hydrogen Production Systems

## Slide 5: A Hydrogen Fuel Cell
A hydrogen fuel cell is the most reversible and popular device that has been used in fuel cell vehicles.
It consumes hydrogen and oxygen and only produces water vapor and heat as exhaust products.
Therefore, a hydrogen fuel cell vehicle produces zero tailpipe greenhouse gas (GHG) emission.
In general, hydrogen is produced using either steam methane reforming or electrolysis of water.
The adoption of FCEVs would significantly reduce a country’s dependence on foreign oil and Carbon release.

## Slide 6: Hydrogen: The Primordial Bestower to The Ecosystem
On the ecosystem scale, hydrogen supports microbial communities in most terrestrial, aquatic, and host-associated ecosystems.
This is the primordial electron donor.
In all biological systems, hydrogen metabolism is the most superior energy generator.
Better understanding of hydrogen metabolism is the backbone of future renewable energy.
A ‘mole of electrons’ is 6.022 × 1023 electrons.
The charge (F) is N · e, where e is 1.602 × 10−19 C.
F = N · e = 96485 C

## Slide 7: The Atomistic Hydrogen Metabolism
Most irreversible metabolism is combustion of hydrogen.
Hydrogen gas forms explosive mixtures with air in concentrations from 4–74%.
The explosive reactions may be triggered by spark, heat, or sunlight.
A controlled Combustion is used in Next generation Hydrogen DI-SI I.C. Engines.

## Slide 8: The Holistic Art of Hydrogen Metabolism
Microorganisms conserve energy by metabolizing hydrogen.
Oxidation of this high-energy fuel yields electrons that can be used for respiration and carbon-fixation.
Electrochemical reaction of Hydrogen is the most reversible reaction.
Electrochemical reaction produces electricity
At cathode ½ O2 + 2e-  O2-
At anode H2 + O2-  H2O + 2e-
Overall reaction H2+ ½ O2  H2O
It is the change in this Gibbs free energy of formation,Gf, that generates electrical energy.
A fuel cell only can convert this change in Gibbs free energy into electrical energy.

## Slide 9: Change in Gibbs Free Energy
If the fuel cell is a ‘reversible’ device, then all this Gibbs free energy is converted into electrical energy.

## Slide 10: Electrical Energy Generated by An Ideal Fuel Cell
In the hydrogen fuel cell, two electrons pass round the external circuit for each molecule of hydrogen consumed.
Therefore, for one mole of hydrogen used, 2N electrons pass round the external circuit – where N is Avogadro’s number.
If −e is the charge on one electron, then the charge that flows is
If E is the voltage of the fuel cell, then the electrical work done moving this charge round the circuit is
Electrical work done = charge  voltage = -2F.V Joules.

## Slide 11: Ideal Cell Voltage
If the system is reversible (or has no losses), then this electrical work done will be equal to the Gibbs free energy released.
This fundamental equation gives the electromotive force (EMF) or reversible open circuit voltage of the hydrogen fuel cell.
In practice the voltage would be lower than this because of the voltage drops in the circuit elements.
Some of the irreversibilities apply a little even when no current is drawn, so even the OCV of a fuel cell will usually be lower.

## Slide 12: Ideal Fuel Cell Capacity
The “ideal” efficiency of a reversible galvanic cell is related to the enthalpy for the cell reaction by
ηid will be 100% if the electrochemical reaction involves no change in the number of gas moles, that is, when ΔS is zero.

## Slide 13: The Fundamental Law : Electrochemical Reaction
In a fuel system, generating chemical energy into electrical energy can be done by transforming hydrogen and oxygen into steam were restricted by efficiency limits of the Carnot thermal cycle.
(Larminie and Dicks 2000)

## Slide 14: Second Law Analysis of Fuel Cell

## Slide 15: Flow Diagram for a Fuel Cell System

## Slide 16: Fuel Cell Technologies
There are six major types of fuel cells depending on the type of their electrolyte.
Proton exchange membrane (PEM) or Polymer exchange membrane fuel cells (PEMFCs)
Alkaline fuel cells (AFCs)
Phosphoric acid fuel cells (PAFCs)
Molten carbonate fuel cells (MCFCs),
Solid oxide fuel cells (SOFCs)
Direct methanol fuel cells (DMFCs)

## Slide 17
V
AFC
PEMFC
PAFC
MCFC
SOFC
H2
OH -
Fuel
H2O
H2
H +
DMFC
H +
H +
O 2-
CO3 2-
600C 100 kW
600C 250 kW
1900C 11 MW
6500C 2 MW
10000C 1 MW
800C 2 MW
O2
O2
H2O
O2
H2O
O2
H2O
O2
CO2
O2
CH3OH
CO2
H2
H2
H2O
H2O
H2
Anode
Electrolyte
Cathode
Oxygen
e
Max attained
production
Classification based on electrolyte used

## Slide 18: Fuel and Energy Flow Diagram of A Fuel Cell

## Slide 19: Fuel Cell Electric Prime Mover

## Slide 20: Fuel Cell Vehicles
Electric vehicles that use fuel cells in their power train are often called fuel cell vehicles.
If fuel cells are the only source of power in the vehicle then the configuration is a non-hybrid fuel cell vehicle.
This vehicle has a fuel cell to provide electric power, a DC/DC convertor to boost up the low output voltage of the fuel cell.
An inverter to feed the required waveforms to the electric motor.

## Slide 21: Optimal Operation of Fuel Cell
Like other prime movers, fuel cells have an optimum operating point.
The Optimum point generates maximum efficient power and increases the fuel-economy.
The best design is the one that gives maximum power to the system while maintaining the optimal operating point of the fuel cell.

## Slide 22: Load Vs Performance of A Fuel Cell
The instantaneous power demanded by a vehicle has a huge impact on operation of the fuel cells.
To meet the demand in non-hybrid fuel cell vehicles, the nominal power of the fuel cell is chosen at the maximum possible power of the vehicle.
Therefore, the real driving conditions may not let the the fuel cell to operate in optimal conditions,
Urban driving cycle leads to generation of lower loads on a huge fuel cell.

## Slide 23
Performance characteristics of a single Fuel Cell

## Slide 24: Hardware Configuration of a typical fuel cell Drive
accelerator pedal
brake pedal
vehicle controller
peaking
power sound
6: electronic interface;
7: motor controller;
8: traction motor;
9: transmission;
10: wheels.

## Slide 25: Performance of Fuel Cell-alone-powered Drive Train : City Driving
20
40
60

## Slide 26: Configuration of a typical fuel cell Hybrid Drive
Battery
Regenerative Brake

## Slide 27: List of Control Parameters

## Slide 28: Flow chart of the control strategy

## Slide 29: Performance of Fuel Cell-Hybrid-powered Drive Train : City Driving

## Slide 30: Optimal Operation of Fuel Cell

## Slide 31: The main challenges in adopting Fuel Cell (FC) technologies