## Slide 1: Analysis of Turbulent (Infected by Disturbance) Flows
Quantification of the Infection & its Effect on Heat Transfer Potential....
P M V Subbarao
Professor
Mechanical Engineering Department
I I T Delhi

## Slide 2: Strategic Realization of Newton’s Cooling of PCBs

## Slide 3
The convection systems studied so far are laminar and, as such, are destined to exist only under special circumstances.
It is common knowledge—a fact reinforced daily by direct observations—that laminar flows can come undone and breakdown to a seemingly more complicated flow called turbulence.
In convective heat transfer research, however, the study of transition is important because the heat transfer potential of a turbulent flow differs vastly from that of its laminar counterpart.
The special circumstances necessary for the transition from analytically predictable laminar flows to analytically unpredictable turbulent f lows
Initial Remarks

## Slide 4: The Overshadowed Ultimate Truth
In an 1854 paper, Hagen noted that the difference between laminar and turbulent flow was clearly visible in the efflux jet.
This jet was either “smooth or fluctuating,” and in glass tubes, where sawdust particles either “moved axially” or, at higher Q, “came into whirling motion.”
Thus Hagen was a true pioneer in fluid mechanics experimentation.
Unfortunately, his achievements were somewhat overshadowed by the more widely publicized 1840 tube-flow studies of J. L. M. Poiseuille, the French physician.

## Slide 5
Reynolds Studies on Viscous Flow with very low to High Inertial Force

## Slide 6: Laminar-Turbulent Transition

## Slide 7: Receptivity of Pipe Flow to Ambient Disturbances

## Slide 8: Can a given physical state withstand a disturbance and still return to its original state?

## Slide 9: Stability of a Physical State
Stable
Unstable
neutral stability
Stable for small disturbances but unstable for large ones

## Slide 10
The equations of Convection Heat Transfer proved that every convection system will have exclusive Velocity and temperature Profiles.
Stability of Convection System ???
If the flow is disturbed, will the disturbance gradually die down, or will the disturbance grow such that the flow departs from its initial profiles and never recovers???
The Instability of Convection Systems

## Slide 11: The perturbation of Velocity Field
Define and introduce a 2D perturbation velocity vector into 2D Modulation Equations:
The components of the perturbation velocity are obtained from the stream function as:
Introduce the disturbance velocities into stability equations:
=

## Slide 12: Orr-Sommerfeld -equation
The Orr-Sommerfeld -equation was derived by Orr and independently Sommerfeld .
This equation is obtained by Introducing disturbance velocity functions into modulation equations .
Eliminate the pressure terms by differentiating the first component of the equation with respect to y and the second with respect to x respectively and subtracting the results from each other.
This constitutes the fundamental differential equation for stability of laminar flows in dimensionless form.

## Slide 13: Orr-Sommerfeld Eigen value Problem
The Orr-Sommerfeld equation is a fourth order linear homogeneous ordinary differential equation.
With this equation the linear stability problem has been reduced to an eigenvalue problem. :
OSEV Equation contains the main flow velocity distribution U(y) which is specified for the particular flow motion under investigation, the Reynolds number, and the parameters , cr, and ci .

## Slide 14: Solution of OS Equations
The Orr-Sommerfeld equation is an eigenvalue problem .
To solve this differential equation, first of all the velocity distribution must be specified.
As an example, the velocity distribution for plane Poisseule flow can be prescribed.
For given Reynolds number and the wavelength, OSE with the boundary conditions provide one eigen function (y) and one complex eigen value c=cr+ici with
as the phase velocity of the prescribed disturbance.

## Slide 15: Recognition of Stability of Flow
For a given value of  disturbances are damped if ci <0 and stable laminar flow persists.
ci > 0 indicates a disturbance amplification leading to instability of the laminar flow.
The neutral stability is characterized by ci = 0.
For a prescribed laminar flow with a given U(y) the results of a stability analysis is presented schematically on a Re Vs frequency of disturbance.
c=cr+ici

## Slide 16: Stability Condition for a plane Poiseuille Flow
Disturbance

## Slide 17: Effect of pressure gradient
Negative values of pressure gradient signify a favourable pressure gradient.
positive values signify an adverse pressure gradient (pressure increasing downstream),

## Slide 18: Major Classes of Instability
Wall-bounded Convection Systems:
  Boundary layers, pipe flows, etc.
  Any general convection system non-inflexion point velocity profile.
  viscosity plays a role
  sensitive to the form of the basic flow
Free-shear flows:
  mixing layers, wakes, jets, etc
  less sensitive to the form of the basic flow
  Viscosity is not responsible.

## Slide 19: Stability of Blasius BL

## Slide 20: Sketch of transition process in the boundary layer along a flat Plate
Fluid Mechanics for Engineers, A Graduate Textbook, Meinhard T. Schobeiri, 2010.
A stable laminar flow is established that starts from the leading edge and extends to the point of inception of the unstable two-dimensional Tollmien-Schlichting waves.

## Slide 21: Sketch of transition process in the boundary layer along a flat Plate
z
Location 1: Stable Laminar Zone

## Slide 22: Sketch of transition process in the boundary layer along a flat Plate
z
Location 2: Onset of the unstable One -dimensional Tollmien-Schlichting waves.
Laminar Flow fighting against the Disturbances

## Slide 23: An intermittently laminar-turbulent flow

## Slide 24: Intermittency Factor

## Slide 25: Sketch of transition process in the boundary layer along a flat Plate
z
Location 3: Onset of the unstable two-dimensional Tollmien-Schlichting waves.

## Slide 26: Sketch of transition process in the boundary layer along a flat Plate
z
Location 3+: Bursts of turbulence in places with high vorticity

## Slide 27: Sketch of transition process in the boundary layer along a flat Plate
z
Location 3++Intermittent formation of turbulent spots (Horseshoe) with high vortical core at intense fluctuation.

## Slide 28: Transition process along Flow Direction on A flat plate

## Slide 29: Hans Albert Einstein (May 14, 1904 – July 26, 1973)
Hans Albert Einstein an avid sailor, frequently taking colleagues and family out for excursions on the San Francisco Bay.
On his many field trips and academic excursions, he took thousands of pictures, many of which he developed himself and presented as slide shows.
In 1988, the American Society of Civil Engineers created the Hans Albert Einstein Award to recognize outstanding achievements in erosion control, sedimentation and/or waterway development.

## Slide 30: Sketch of transition process in the boundary layer along a flat Plate
z
Location 4: Development of unstable, three-dimensional waves and the formation of vortex cascades
Laminar Flow Accepting the Disturbances

## Slide 31: Sketch of transition process in the boundary layer along a flat Plate
z
Zone 5: Coalescence of turbulent spots into a fully developed turbulent boundary layer.

## Slide 32: Sketch of transition process in the boundary layer along a flat Plate
Fully Developed Turbulent Zone
z
Fully Developed Turbulent Flow

## Slide 33: Definition of A Turbulent Flow
A Fluid motion in which velocity, pressure, and other flow quantities fluctuate irregularly in time and space.
“Turbulent Fluid motion is an irregular condition of flow in which the various quantities show a random variation with time and space coordinates, so that statistically distinct average values can be observed.” - Hinze
“Turbulence is due to the formation of point or line vortice on which some component of the velocity becomes infinite.:” -Jean Leray

## Slide 34: 2-D Turbulent Boundary Layer Convection Heat Transfer

L

## Slide 35: First Method of Analyzing Steady Turbulent Convection System
Reynolds (1895) decomposed the field variable into a time average
variable and a turbulent fluctuation
- Likewise
f stands for any scalar: u, v, w, T, p, where:
Time averaged Scalar
is a random variable with zero mean value

## Slide 36: Average and Fluctuating Flow Properties
Instantaneous velocity
Average
velocity
fluctuation
around
average
velocity
time
T
Local velocity
Average
velocity
fluctuation
around
average
velocity
x

## Slide 37: Averaging of Continuity Equations
Substitute Reynolds Decomposition into continuity equation:

## Slide 38: Averaging of Continuity Equations
Continuity equation for an Infected flow:
Consider Reynolds Averaging of An Infected continuity equation:

## Slide 39: Time Averaging Operations

## Slide 40: Reynolds Averaging of Energy Equation
The general Energy conservation Equation of an Infected Convection System:
T

## Slide 41: Method of Reynolds Averaging
Reynolds Averaging of
Similarly

## Slide 42: Method of Reynolds Averaging
Reynolds Averaging of

## Slide 43: Reynolds Averaged Energy Equation for Convection
The general Energy conservation Equation
Reynolds Averaging gives:

## Slide 44: Reynolds Heat Flux Vector
This is usually called the Reynolds/Eddy Heat Flux vector.
Fourier’s Constitutive Equation for the Heat Flux
=
=

## Slide 45: Reynolds Averaged Energy Equation for Turbulent Convection
The general Averaged Energy conservation Equation for turbulent convection
The Big question is :
If the products , and survive the time-averaging
process, that is, if they are nonzero, are they negative or positive?

## Slide 46: Averaging of x-momentum Equation
Write x-momentum equations in a short format:
Reynolds decomposition of turbulent flow variables:

## Slide 47
+
Reynolds Averaging of x-momentum Equation
+

## Slide 48
Reynolds Averaging of x-momentum Equation

## Slide 49: Reynolds Averaged Steady Turbulent Momentum Equations
Reynolds averaged x-momentum equation for steady incompressible turbulent flow

## Slide 50
Reynolds averaged y-momentum equation for steady incompressible turbulent flow
Reynolds averaged z-momentum equation for steady incompressible turbulent flow
Reynolds Averaged Steady Turbulent Momentum Equations

## Slide 51: Reynolds Averaged Equations for Forced Convection

## Slide 52: Reynolds Stress Tensor
This is usually called the Reynolds stress tensor
Reynolds stresses : total 9  6 are unknown

## Slide 53
Time averaged Infected Navier Stokes Equation
For all the Three Momentum Equations, total turbulent stress tensor:

## Slide 54: Reynolds stresses & Heat Fluxes
Performing the Reynolds Averaging Process, new terms has arisen, namely the Reynolds-stress tensor:
This brings us at the turbulent closure problem, the fact that we have more unknowns than equations.
  Three velocities + pressure + six Reynolds-stresses+Temperature + three Rynolds heat flux
  Three momentum equations + the continuity equation+the energy equation
To close the problem, we need additional equations to solve infected flow.

## Slide 55: Prandtl Mixing Length Hypothesis
X
Y
y
The fluid particle A with the mass dm located at the position , y+lm and has the longitudinal velocity component U+U is fluctuating.
This particle is moving downward with the lateral velocity v and the fluctuation momentum dIy=dmv.
It arrives at the layer which has a lower velocity U.
According to the Prandtl hypothesis, this macroscopic momentum exchange most likely gives rise to a positive fluctuation u >0.