## Slide 1: Governing Equations for Convection Heat Transfer
P M V Subbarao
Professor & Head
Mechanical Engineering Department
Generalized Mathematical Models to predict Temperature Field…
Physics is experience, arranged in economical order.
— Prof. Ernst Mach

## Slide 2: Fourier’s Constitutive Equation for the Heat Flux: 1802
The Fourier Conduction Equation:

## Slide 3
This dimensionless temperature gradient at the wall is named as
Nusselt Number:
Local Nusselt Number
Nusselt's Clue to handle Convective Heat Transfer System

## Slide 4: Order of Merit of A Convective Heat Transfer in a System
Field Synergy Principle:
Guo et al. (1998) analyzed the physics behind the occurrence of Convection heat transfer.
This helped in explaining the all possibilities of increasing the convective heat transfer.
They proposed that the non-dimensionalized form of local balance between conduction and convection in any flow system.
This can be written as:
The actual value of heat transfer coefficient is decided by the local orientation of streamlines and isotherms.
Any innovation which tries to align streamlines more orthogonal to isotherms will generate high value of heat transfer coefficient.

## Slide 5: Impact of Flow Channel Geometry on Convection Heat Transfer

## Slide 6: Transverse vs Longitudinal Flow thru Pillows

## Slide 7: Rate Equations for Laws of Nature for A Thermodynamic Control Mass
Conservation of Mass :
Conservation of Momentum :
First law of thermodynamics :
Control Mass

## Slide 8: Tools for Comprehensive Description
The conservation laws are (strictly speaking), valid only for closed systems (Control Mass).
Convection Systems are open systems (Control Volumes), where the mass flow continuously crosses the system boundary.
Application of the conservation laws to CVs demand a special mathematical tool.
These tools help in estimation of resultant force generated by an arbitrary field quantity g(, t).

## Slide 9: Camp Fire As A Control Volume

## Slide 10: Wind Turbine As A Control Volume

## Slide 11: Wind Systems Interacting with A Wind Turbine

## Slide 12: Energetics of A Fluid Parcel across An Open System
x
z
y
Cold undeformed State
Warm deformed State

## Slide 13
Reynolds Control Volume

## Slide 14
Biologically Inspired Reynolds Control Volume

## Slide 15
Reynolds Control Volume for Convective Mass Transfer System

## Slide 16: Reynolds Description of a Flow System
Every fluid system must be treated as “The control mass.”
Consider a simple Fluid System that occupies region I and region II) at time t0.
Fluid particles of region – I are trying to enter Region – II (Control Volume) at time t0.
I
II
At time t0

## Slide 17: Reynolds Thinking about a Flow System
The same fluid system transforms to regions (II+III) after a time dt.
I
II
At time t0
II
III
At time t0+dt
Fluid particles of region-I fully entered CV (Region-II) in a time dt.
Few other fluid particles which were belonging to CV at t0 are trying exit CV and occupy III at time t0 + dt.
Why and How?????

## Slide 18: Reynolds Description of A Control Volume
At time t0
At time t0+dt

## Slide 19
The control volume may move as time passes.
I
II
At time t0
II
III
At time t0+dt
I is trying to enter CV at time t0
I has entered and III has left CV at time t0+dt
Reynolds Descriptions of a Convection System

## Slide 20: Actions on Fluid Parcel across A Flow System
x
z
y
Cold undeformed State
Warm deformed State

## Slide 21: The Field Variable
Any field quantity g(,t) may be a zeroth, first or second order tensor valued function.
Namely, as mass, concentration, energy, charge, velocity vector, and stress tensor.
A fluid parcel of given initial volume (dV0) may change its volume and/or change it surface (ds0) with a given time, while moving through the flow field.
This is due to various experiences by this fluid parcel, namely, dilatation, compression, deformation, heating/cooling and oxygenation or …..
Let us consider all the fluid parcels at any time and therefore, it is called the material volume, and the total field quantity is defined as:

## Slide 22: Change in Field quantity of A Convection System
The total value of a field quantity for a CV.
volume integral of the quantity g(,t):
This is a function of time only.
The integration must be carried out over the varying volume V(t).
The material change of the quantity G(t) is expressed as:
Since the shape of the volume V(t) changes with time, the differentiation and integration cannot be interchanged.

## Slide 23: Need for A Generalized Leibniz Integral Rule
Osborne Reynolds (1842–1912), developed a three-dimensional generalization of the Leibniz integral rule.
It is used to recast time derivatives of integrated quantities and is useful in formulating the basic conservation equations for control volumes.
This is known as Reynolds Transport Theorem.

## Slide 24: Energetics of a differential volume at different instants of time

## Slide 25: The Fundamental Reynolds Analogy (Algorithm)
Reynolds analogy permits the transformation of the time dependent volume V(t) into the fixed volume V0 at time t = 0 by using the Jacobian transformation function:

## Slide 26
With this operation it is possible to interchange the sequence of differentiation and integration:
The chain differentiation of the expression within the parenthesis results in
Change in Field quantity of A Convection System

## Slide 27: Material Derivative of Jacobian Function
Every volume element dV follows the motion from x=f(, t) to x=f(, t+dt) and changes its shape and size.
As a result, the Jacobian transformation function undergoes a time change.
This change is the material derivative of J:

## Slide 28
Introducing the material derivative of the Jacobian function and simplifying based on derivatives of transformation functions
Transformation Function for CM to CV
The chain rule applied to the second and third term yields:

## Slide 29
The Reynolds transformation permits the back transformation of the fixed volume integral into the time dependent volume integral.
Transformation Function for CM to CV

## Slide 30
The second volume integral in above equation can be converted into a surface integral by applying the Gauss' divergence theorem:
Result of Reynolds Transformation

## Slide 31: Engineering Mathematics of Reynolds Transport Theorem
G is any property of the flow system (mass, energy, momentum, enthalpy, etc.).
Define = dG/dm as the intensive value, or the amount of G per unit mass in any small element of the fluid.
The total amount of G in the control volume is thus

## Slide 32
This Equation is valid for any system boundary with time the dependent volume V(t) and surface s(t) at any time.
Also valid at the time t = t0 , where the volume V = VC and the surface s = sC.
VC and sC are named as control volume and control surface.
These control surfaces can be inlets or outlets.
Engineering Use of Reynolds Transformation

## Slide 33
Application of RTT to A Natural CV

## Slide 34
Engineering Use of Reynolds Transformation
Inflow
outflow

## Slide 35
Vectorial Recognition of Inflow & Outflow
Inflow
outflow