## Slide 1: Solution of Convection Heat Transfer Equations : Flat Plate Boundary Layer
Application of Mathematical Tricks by Blasius to Prandtl’s Intuition…
P M V Subbarao
Professor & Head
Mechanical Engineering Department

## Slide 2
Intuition of SIMILARITY Variable
For a solution obeying similarity in the velocity profile must have
where f & G are universal functions, independent of x (position along the plate).
Best trick by Blasius lead to finalize a model for similarity form for a value of
Note that  is a dimensionless variable.
Since Blasius had a reason to believe that for a slowly growing FPBL

## Slide 3
GDEs for Master Profiles in Laminar Boundary Layer Convection on A Flat Plate
Is it possible to guess Simple form of above functions?
Fluid Mechanics as A Puzzle Game!
Developed by Paul Richard Heinrich Blasius in 1908 as a student of Ludwig Prandtl
The truth of boundary layer physics is
F & G are (similarity functions) master functions of stream functions and temperature, respectively.
Both are scalar functions….
FPBL Momentum Equation:
FPBL Thermal Energy Equation:

## Slide 4
Discovery of Similarity Variable by The Method Of Guessing
Blasius wanted that above GDE to generate a stream function to give a velocity u = /y satisfying the similarity variable
so that
So, he started-off by guessing
where F is a similarity function.
Will it work ????
Lets see…..
Along with a similarity function for velocity profile

## Slide 5
Is it a right Guess ?
First guess of Blasius
not OK
OK
then he obtained
This form does not satisfy the condition that u/U is a function of  alone.
Similarity demands the first derivative F’() is to be a function of  alone, but not F.
But Blasius noted that the extra function is (Ux)-1/2!
So his first guess failed because of the term (Ux)-1/2.
Used this nuisance term to generate a better guess.

## Slide 6
Second Guess learnt from the first Guess
Second Guess
Now remembering that x and y are independent of each other and recalling the evaluation of /y,
Thus, the first guess helped in guessing the correct function.
This new form of  that satisfies similarity in velocity!
But this does not mean that the job was completed.
Need to complete the description of the function F().

## Slide 7
Second Guess: Similarity Function for 
A set of basic derivatives of similarity variable are necessary to obtain the function F() :

## Slide 8
The next steps involve tedious differential calculus, to evaluate the terms in the BL Stream Function equation.
Conversion of Third Order PDE into ODE
The third order Partial derivative is:

## Slide 9
Blasius worked out the two second order derivatives:
Conversion of Second Order PDs into ODs

## Slide 10
Development of Master ODE for Stream function

## Slide 11: ODE governing Flat Plate BL
This is known as Blasius Boundary Layer Equation

## Slide 12: Energy Equations for 2-D Boundary Layer Convection Heat Transfer: PDE to ODE
The Similarity Function for Non-dimensional Temperature:

## Slide 13: Energy Equations for 2-D Boundary Layer Convection Heat Transfer: PDE to ODe

## Slide 14: Energy Equations for 2-D Boundary Layer Convection Heat Transfer: PDE to ODe

## Slide 15: ODE for Master temperature Profile for 2-D Boundary Layer Forced Convection Heat Transfer

## Slide 16: 2-D Boundary Layer Convection Heat Transfer: ODEs for Master Profiles
Master Stream Function Equation for Boundary Layer:
Master Temperature Equation for Boundary Layer:

## Slide 17
The boundary conditions in terms of 
BOUNDARY CONDITIONS for Master Profiles
The boundary conditions in terms of F
The boundary conditions for G

## Slide 18: ODE for Master Profile of Momentum Boundary Layer: The Blasius Equation
The Blasius equation with the boundary conditions exhibits a boundary value problem.
However, the location of one boundary is unknown, though boundary condition is known.
However, using an iterative method, it can be converted into an initial value problem.
Assuming a certain initial value for F=0, Blasius equation can be solved using Runge-Kutta or Predictor- Corrector methods

## Slide 19: Solution of Momentum Blasius Equation
Integrate above equation to get:
=
Integrate above equation again

## Slide 20: Solution of Momentum ODE of BL
Use the boundary condition:
Use the other boundary condition:

## Slide 21: Solution of Momentum ODE of BL
Carry out final integration to get equation for F:

## Slide 22: An Iterative Solution to Velocity BL
Choose a large η (e.g., ηmax = 20), and divide it into a number of intervals, ηi.
Guess the distributions for f ′ and f [e.g., f (η) = η, f ′(η) = 1].
Calculate, at each ηi, for all values of η between 0 and ηmax.
Calculate,
Calculate f ′′ at every ηi.
Calculate f ′ at every ηi.
Calculate f at every ηi.
Using f and f ′ distributions, go to step 3 and repeat the procedure until convergence is achieved at every η.

## Slide 24: Iterative Solution Data
 F F' F''
0 0 0 0.33206
0.1 0.00166 0.03321 0.33205
0.2 0.00664 0.06641 0.33199
0.3 0.01494 0.0996 0.33181
0.4 0.02656 0.13277 0.33147
0.5 0.04149 0.16589 0.33091
0.6 0.05974 0.19894 0.33008
0.7 0.08128 0.23189 0.32892
0.8 0.10611 0.26471 0.32739
0.9 0.13421 0.29736 0.32544
1 0.16557 0.32978 0.32301
1.1 0.20016 0.36194 0.32007
1.2 0.23795 0.39378 0.31659
1.3 0.27891 0.42524 0.31253
1.4 0.32298 0.45627 0.30787
1.5 0.37014 0.48679 0.30258
1.6 0.42032 0.51676 0.29667
1.7 0.47347 0.54611 0.29011
1.8 0.52952 0.57476 0.28293
1.9 0.5884 0.60267 0.27514
2 0.65003 0.62977 0.26675

## Slide 25
2.2 0.7812 0.68132 0.24835
2.3 0.85056 0.70566 0.23843
2.4 0.9223 0.72899 0.22809
2.5 0.99632 0.75127 0.21741
2.6 1.07251 0.77246 0.20646
2.7 1.15077 0.79255 0.19529
2.8 1.23099 0.81152 0.18401
2.9 1.31304 0.82935 0.17267
3 1.39682 0.84605 0.16136
3.1 1.48221 0.86162 0.15016
3.2 1.56911 0.87609 0.13913
3.3 1.65739 0.88946 0.12835
3.4 1.74696 0.90177 0.11788
3.5 1.83771 0.91305 0.10777
3.6 1.92954 0.92334 0.09809
3.7 2.02235 0.93268 0.08886
3.8 2.11604 0.94112 0.08013
3.9 2.21054 0.94872 0.07191
 F F' F''

## Slide 26
4 2.30576 0.95552 0.06423
4.1 2.40162 0.96159 0.0571
4.2 2.49806 0.96696 0.05052
4.3 2.595 0.97171 0.04448
4.4 2.69238 0.97588 0.03897
4.5 2.79015 0.97952 0.03398
4.6 2.88827 0.98269 0.02948
4.7 2.98668 0.98543 0.02546
4.8 3.08534 0.98779 0.02187
4.9 3.18422 0.98982 0.0187
5 3.2833 0.99155 0.01591
5.1 3.38253 0.99301 0.01347
5.2 3.48189 0.99425 0.01134
5.3 3.58137 0.99529 0.00951
5.4 3.68094 0.99616 0.00793
5.5 3.7806 0.99688 0.00658
 F F' F''

## Slide 27
5.6 3.88032 0.99748 0.00543
5.7 3.98009 0.99798 0.00446
5.8 4.07991 0.99838 0.00365
5.9 4.17976 0.99871 0.00297
6 4.27965 0.99898 0.0024
6.1 4.37956 0.99919 0.00193
6.2 4.47949 0.99937 0.00155
6.3 4.57943 0.99951 0.00124
6.4 4.67939 0.99962 0.00098
6.5 4.77935 0.9997 0.00077
6.6 4.87933 0.99977 0.00061
6.7 4.97931 0.99983 0.00048
6.8 5.07929 0.99987 0.00037
6.9 5.17928 0.9999 0.00029
7 5.27927 0.99993 0.00022
 F F' F''

## Slide 28
7.1 5.37927 0.99995 0.00017
7.2 5.47926 0.99996 0.00013
7.3 5.57926 0.99997 9.8E-05
7.4 5.67926 0.99998 7.4E-05
7.5 5.77925 0.99999 5.5E-05
7.6 5.87925 0.99999 4.1E-05
7.7 5.97925 1 3.1E-05
7.8 6.07925 1 2.3E-05
7.9 6.17925 1 1.7E-05
8 6.27925 1 1.2E-05
8.1 6.37925 1 8.9E-06
8.2 6.47925 1 6.5E-06
8.3 6.57925 1 4.7E-06
8.4 6.67925 1 3.4E-06
8.5 6.77925 1 2.4E-06
8.6 6.87925 1 1.7E-06
8.7 6.97925 1 1.2E-06
8.8 7.07925 1 8.5E-07
 F F' F''

## Slide 29: Nature of Master Thermal Profile Equation
The master momentum function is known to us.
It is important to understand the interaction between Pr and on behaviour of Master Temperature Profile.

## Slide 30: ODE for Master Profile of Thermal Boundary Layer
In general (for any Pr), above equation can be integrated, keeping in mind that F(η) is a known function available in tabular form
ln

## Slide 31: Master Profile of Thermal Boundary Layer
The boundary conditions for G
ln
If is known by any other means:
Integrating above equation again from 0 to η yields

## Slide 32: Master Profile of Thermal Boundary Layer
The boundary conditions for G
Use the wall boundary condition to get
The solution for G(η) above depends on an unknown constant of integration, (0), because the free-stream condition has not been used yet.

## Slide 33: Master Profile of Thermal Boundary Layer
The boundary conditions for G
Use the free stream boundary condition to get:

## Slide 34: Master Profile of Thermal Boundary Layer
The solution is now complete.
Master Temperature profiles for different Prandtl Number can be generated using above equation.

## Slide 35: Master Temperature Profile for FP Boundary Layer

## Slide 36: Estimation of Local Heat Transfer Coefficient Using Master Profiles
The value of (0) is the most important information for calculating convection heat transfer coefficient.
Recall the local application of Newton’s law of wall cooling.

## Slide 37: Stream Function and Temperature Profiles
The stream function on a Flat Plate with Laminar Forced Convection Cooling is:
;
Similarly the non-dimensional Temperature profile is:

## Slide 38: Role of Prandtl Number on Cooling Behaviour of Fluids
y
x
For large Pr (oils):
Pr > 1000
y
x
For small Pr (liquid metals):
Pr < 0.1
Fluid viscosity greater than thermal diffusivity
Fluid viscosity less than thermal diffusivity

## Slide 39: Master Profile of Low Prandtl Number Thermal Boundary Layer
Alternate method is required for fluids having Pr below 0.5.
Generally liquid metals have low value of Prandtl number.
Separate solutions are required to evaluated for master profile equation.
In general an analytical replacement for the Nu of all the fluids with the limit Pr → 0.
In highly conductive fluids the velocity boundary layer is much thinner than the thermal layer.
Therefore, in this limit it is permissible to set F = 1 in most of the thermal boundary layer.

## Slide 40: Master Profile of Low Prandtl Number Thermal Boundary Layer
Master profile for Thermal Boundary Layer of low Pr.
This equation leads to an explicit solution for G(η):
Further integration to get an explicit solution for G(η):

## Slide 41: Experimental Study
How to set up an experimental test?
Let’s say you want to know the heat transfer rate of an airplane wing (with fuel inside) flying at steady conditions………….
What are the parameters involved?
  Velocity, –wing length,
  Prandtl number, –viscosity,
  Nusselt number,
Which of these can we control easily?
Looking for the relation using Principle of Similitude:

## Slide 42: Experimental Studies to Develop Empirical Correlation
Insulation
L
At steady state electrical power input to the heater is equal to rate of total cooling (Convection Heat Transfer) by surrounding fluid.
Measure current (hence heat transfer) with various fluids and test conditions.
Fluid properties are typically evaluated at the mean film temperature