## Slide 1: Deliberations on Force Vector System
P M V Subbarao
Professor & Head
Mechanical Engineering Department
Vitality Means More to Explore ……..

## Slide 2: Moment as The cross product
In two dimensional and three-dimensional spaces.
The moment of about point A may be represented as
where is a position vector which runs moment reference point A to any point on the line of action of .
The magnitude of this expression is
= sin.
Sense and direction of is established by the righthand rule.

## Slide 3: Moment as The cross product
The sequence would produce a vector with a sense opposite to that of the correct moment
If and are not perpendicular and are easily expressible in vector notation, then the cross-product expression is often preferable

## Slide 4: Varignon Theorem
One of the most useful principles of mechanics is Varignon’s theorem
It states that the moment of a force about any point is equal to the sum of moments of the components of the force about the same point
Proof of this theorem:
Consider the force acting in the plane of the body as shown in Figure
The forces and represents any two rectangular components of .
The moment of about O is

## Slide 5: Varignon Theorem
Proof :
The forces and represents any two rectangular components of .
The moment of about O is
Because
it may be written as
Using the distributive law for cross product,
Which says that the moment of about O equals the
Sum of the moments about O and its component and

## Slide 6: Efficacy of Varignon Theorem
The moment of about O is .
However, if d is more difficult to determine
d
q
p
Then determine p and q and compute the moment as
Where we take the anti-clockwise moment sense to be positive

## Slide 7: Efficacy of Varignon Theorem
Consider a body with multile forces acting on the body.

## Slide 8: Force Couples
The moment produced by two equal, opposite and non-collinear force is called a couple.
To produce upward rotation of the scapula, or shoulder blade when raising our arms
4 major muscles: Serratus anterior, Lower trapezius, Upper Trapezius, Levator Scapula generate Force couples.
Consider the action of two equal and opposite force and – a distance d apart

## Slide 9: Force Couples
These forces cannot be combined into a single force because their sum in every direction is zero
Their only effect is to produce a tendency of rotation.
The combined moment of the two forces about an axis normal to their plane and passing through any point such as O in their plane is the couple
The couple has a magnitude
=
=
The direction is counterclockwise when viewed from the above
Note the magnitude of the couple is independent of the distance a.

## Slide 10: Force Couple : Vector Algebra Method
A
B
& are position vectors which run from point O to arbitrary points A & B,
The combined moment about a point O of the forces forming the couple using vector algebra is given as:
Select arbitrary points A and B on the lines of action of and –, respectively.

## Slide 11: Force Couple : Vector Algebra Method
A
B
is represented by a new vecot
Here again the moment expression contains no reference to the moment center O
Therefore, moment expression is same for all the moment centers
may be classified as a free vector

## Slide 12: Sense of Force Couple

## Slide 13: Equivalent Force Couples
Changing the value of and d does not change a given couple as long as the product remains the same.
Follwoing four different configuration of the same couple

## Slide 14: Force - Couple Systems
Effect of a force-couple together acting on a body:
tendency to push or pull the body in the direction of the force and to rotate the body about any fixed axis which does not intersect the line of the force.
The given force acting at point A is replaced by an equal force at some point B
An equal and opposite force is added at point B without introducing any external effects on the body
Force-couple dual effect can be generated easily by replacing the given force by an equal parallel force and a couple

## Slide 15: Force - Couple systems
Now it can be seen that the original force at A and the equal and opposite one at B constitute the couple .
Thus, the original force at A is replaced by the same force acting at a different point B and a couple, without altering the external effects of the original body
The given force acting at point A is replaced by an equal force at some point B and the counterclockwise couple

## Slide 16: Force in 3D Rectangular (Cartesian) Components Space
+
Direction cosines of
From the Pythagorean theorem
implies
X
Y
Z

## Slide 17: Rectangular (Cartesian) Components in 3D Space
Rectangular Components in 3D
Sometimes useful to remember while solving problems
X
Y
Z

## Slide 18: Simple Method to Determine the components of force in 3D
The direction of a force in 3D can also be described by
Two points on the line of action of the force &
By two angles which orient the line of action

## Slide 19: Simple Method to Determine the components of force in 3D
Then resolve the horizontal component into x and y-components
=cos

## Slide 20: Moment in three dimensions
In 3D robotics, the concepts of moment and force couple are used to analyze and describe how forces cause both translation and rotation.
This enables precise control over robot motion and structural stability.
These concepts are fundamental in statics and dynamics to understand the full effect of forces on a robot's links, joints, and overall system

## Slide 21: Moment in Three Dimensions
The moment of about the axis through O as
Evaluating the Cross Product
The cross-product expression for may be written as
The expansion of the determinant gives

## Slide 22: Moment in Three Dimensions
The scalar magnitudes of these forces
about the positive x-y-z axes

## Slide 23: Moment about an Arbitrary Axis
The expression for the moment of about any axis through O:
The magnitude of is the dot-product
This scalar is the magnitude of of about .
To obtain the vector expression multiply the magnitude by the direction unit vector
the scalar triple product

## Slide 24: Force Couple in Three-Dimensional Space
In figure two equal and opposite forces and is acting on a body.
The vector runs from any point B on the line of action of to any point
A on the line of action of
Points A and B are located by position vectors and from any point O.
The combined moment of the two forces about about O is

## Slide 25: Couples in Three-Dimensional Space
However, = , so that all reference to the moment center disappears
Thus, the moment of a couple is the same at all points.
The magnitude is
Moment of a couple is a free vector
Moment of force about a point (which is also a moment about a defined axis through a point) is a sliding vector whose direction is along the axis

## Slide 26: Couples in Three-Dimensional Space
Couple vectors obey all the rules which given vector quantities
Thus, the couple vector due to and may be added as shown to the couple vector due to and to produce the couple , which in turn can be produced by and
We can replace a force by its equivalent force couple system

## Slide 27: Couples in Three-Dimensional Space
The force acting at point A is replaced by an equal force at point B and the couple
By adding the equal and opposite for and at B, one can obtain the couple compose of – and .

## Slide 28: Resultants in 3D

## Slide 29: Resultants in 3D
In general any system of forces may be replaced by its resultant force and the resultant couple
If force system consists of Concurrent forces:
Zero resultant Momentum.
Parallel Forces :
For a system of parallel forces not all in the same plane the magnitude of the parallel resultant is simply the magnitude of the parallel resultant forces.
The position of its line of action is obtained from the
principle of moments requiring that .

## Slide 30: Reality of Force System In Engineering
The Truth, “concentrated” forces do not exist in any real system.
Every external force applied mechanically to a body is distributed over a finite contact area, however small.
Every Mechanical System is having a Finite non-zero life due to the distributed nature for Force System

## Slide 31: Distributed Nature of Force System
When to account the way force is distributed?
When the forces are applied over a region whose dimensions are not negligible compared with other pertinent dimensions
If on the other hand, we want to find the distribution of internal forces in the material of body near contact location
The contact location will have appreciable internal stresses and strain
In such case, the load is not treated as concentrated but the actual distribution of forces is considered.

## Slide 32: Types Distributed Force System
There are mainly three kind of distribution:
Line Distribution: When a force is distributed along a line as in continuous vertical load supported by a cable. The intensity w of the loading is expressed as force per unit length of line, newtons per meter (N/m)
Area Distribution:
When a force is distributed over an area as with the hydraulic pressure of water against the inner face of the dam.
The intensity is expressed as force per unit area.
This intensity is called pressure for the action of fluid forces
The basic unit for pressure is the newton per square meter (N/m2)

## Slide 33: Types Distributed Force System
Volume Distribution:
A force which is distributed over the volume of a body is called a body force.
The most common body force is the force of gravitational attraction, which acts on all elements of mass in a body.
The determination of the forces on the supports of the heavy cantilevered structure for example, would require accounting for the distribution of gravitational force throughout the structure

## Slide 34: Center of Mass
A body in space, is seen at any point such as A, the body will be in equilibrium under the action of the tension in the cord and the resultant of the gravitational forces acting on all particles of the body.
This resultant is clearly collinear with the direction of gravity,
For all practical purposes these lines of action will be concurrent at a single point G, which is called the center of gravity of the body.
Under the assumption of uniform and parallel force field due to gravitational attraction of the earth
This result in a unique center of gravity