## Slide 1: Axiomatic Analysis of First Law
P M V Subbarao
Professor & Head
Mechanical Engineering Department
I I T Delhi
Analytics for Geometrization of thermodynamics…

## Slide 2: Sequence of Point Sets
The change of form of the system S that takes place during an adiabatic change of state is a prescribed function of time.
In other words: one can prescribe n functions
.
The change of state that goes through them is of a sort that the time like variation of the coordinates of in sequence.
t
Geometrization of thermodynamics…

## Slide 3: An Important Axiom for Work
Consider number of adiabatic change of States between A and B
Initial State
Final State
Maximum Work Path

## Slide 4: Unique Determination of Work
External work whose magnitude is uniquely determined by initial and final state during an adiabatic change of state will have highest value.
Ley us raise a question!
How to find an adiabatic change of state that makes the magnitude of the corresponding external work W uniquely determined by the initial state and the functions alone.
This may be possible, when the velocity with which the system is deformed becomes “infinitely slow.”

## Slide 5: Unique Determination of Work
Mathematical, when the derivatives:
converge uniformly to null, the work W shall go to a definite value in the limit.
A change of state that takes place so slowly that the difference between the actual external work and maximum possible work tends to null is called as a quasistatic change of state.

## Slide 6: Maximum Work Path
Initial State
Final State

## Slide 7: Quasistatic Change of State
If, under a quasi-static change of state, the external work is known as a function of time :
A quasi-static, adiabatic change of state can thus be interpreted as a sequence of equilibrium points, and each quasi-static, adiabatic change of state corresponds to a certain curve in the space of qi.
An Important assumption:
Under any quasi-static change of state, one shall be able to measure the external work W as if the forces that bring about this work were the same as the ones that are necessary to maintain equilibrium.
If the change of state as a sequence of equilibrium points, the forces are, however, functions of only the states.

## Slide 8: Model for Evaluation of W
For a quasistatic change of state, the expression for W must necessarily have the form:
represents a Pfaffian expression:
and the P1, …, Pn mean functions of the q0, q1, …, qn.
The functions Pi can be determined experimentally when, for each state of S.
The forces that must act on the system from the outside in order for equilibrium to exist are measured.

## Slide 9: Maximum Work Path
Initial State
Final State

## Slide 10: Model for First Law
As long it is dealt with quasi-static adiabatic changes of state, one can now give equation of the first law the form:
This relation must be valid for each t the conclusion follows that only curves in the (n+1)-dimensional space of the qi for which the Pfaffian equation:
is satisfied can represent a quasi-static, adiabatic change of state.
Conversely, any curve in the (n+1)-dimensional space of the qi that satisfies above equation can be regarded as a quasi-static, adiabatic change of state in our simple system.

## Slide 11: Geometrization of Quasistatic Adiabatic Change of State
Let a curve segment be given in parametric representation through the equations:
If one now sets: or
in which t means time and , a parameter, then one can introduce adiabatic changes of state that satisfy the equations:
for each prescribed value of .

## Slide 12: Maximum Work Path
Initial State
Final State

## Slide 13: Quasistatic Adiabatic Change of State
For a sufficiently small , a change of state of this sort is now quasi-static and must ultimately satisfy .
By integrating this equation, however, one finds that:
If we substitute:
in equation ,
then for increasing t and sufficiently small , precisely the same curve would have been traversed, but in the opposite sense.
Quasi-static, adiabatic changes of state of a simple system are “reversible.”

## Slide 14: Summary of Simple System
A “simple” system with the (n+1) state coordinates must satisfy the following conditions:
n of its coordinates – e.g., q1, q2, …, qn - are deformation coordinates.
The external work W is not uniquely determined by the initial state and final state of S under adiabatic changes of state.
The totality of all these possible values for W under these assumptions defines a connected set of numbers.
Under “quasi-static” adiabatic changes of state the external work is equal to an integral of a definite Pfaffian expression of the form: