## Slide 1: Caratheodory’s & Kelvin Analyses of Irreversible Cycles
P M V Subbarao
Professor
Mechanical Engineering Department
I I T Delhi
Thermal limits & geometric logic for Real Life Systems!!!

## Slide 2: KP vs AC : Reversible Cycle
For reversible processes (KP) ⇒(AC).
However, irreversible processes also to be studied in Advanced thermodynamics.
These processes are, as the name suggests, processes that can only be realized in a single “time direction”.
If (AC) is false, falsifies (KP).

## Slide 3: KP vs AC : Irreversible Cycle
The intermediate situations of the system in an irreversible process are not equilibrium situations.
If (AC) is false, falsifies (KP) for an irreversible cycle too????

## Slide 4: Engineering Irreversibilities
Fluid friction
Solid friction
Heat Transfer with a finite temperature difference
Electrical resistance
Thermo-chemical Reactions (Combustion)
Unrestrained motion

## Slide 5: Combustion is An Irreversible Process
Reversed burner

## Slide 6: Irreversible Processes
It is well known that real world process are irreversible processes.
These processes that can only be realized in a single “(time) direction”.
Conceptually, thermodynamics is a theory that studies only equilibrium situations.
However, a qualitative analysis of irreversible processes is always possible as thermodynamic initial and final situations of irreversible processes are always equilibrium situations.
Finally, the true meaning of entropy and second law of thermodynamics emerges from irreversible processes.

## Slide 7: Study of an Irreversible Process
In thermodynamic space, irreversible processes cannot be represented as the usual continuous curves.
However, the initial and final states of an irreversible process are well defined.
It is a practice in thermodynamics to represent an irreversible process as a dashed line in thermodynamic space.
This dashed line connects its initial and final states.
It is natural that the relation (KP) ⇒ (AC) for irreversible processes must be evaluated as well.

## Slide 8: Analysis of an Irreversible Process
Construct two irreversible cycles in the same previous thermodynamic space.
The cycles are constructed analogously to that posed for the cycle in the reversible case.

## Slide 9: Analysis of an Irreversible Process
In the cycle : the irreversible process A → B is assumed to be adiabatic, so QA→B = 0.
The reversible process B→C holds on the line where x1 =x1∗ and x2 =x2∗.
 WB→C = 0.

## Slide 10: Analysis of an Irreversible Process
WB→C = 0.
QB→C > 0 thanks to the difference in at B and C.
;
The reversible process C → A is also supposed to be adiabatic, so QC→A = 0.

## Slide 11: Analysis of an Irreversible Process
This closes the cycle .
Note that due to the irreversibility of can only be traversed in the direction A→B→C→A.

## Slide 12: Analysis of an Irreversible Process
Similarly in the cycle : the irreversible process A → C is assumed to be adiabatic as before, so QA→C = 0.
The reversible process C→B holds on the line where x1 =x1∗ and x2 =x2∗.
 WC→B = 0.

## Slide 13: Analysis of an Irreversible Process
WC→B = 0.
QC→B < 0 thanks to the difference in at B and C.
;
The reversible process B → A is also supposed to be adiabatic, so QB→A = 0.

## Slide 14: Analysis of an Irreversible Process
This closes the cycle .
Note that due to the irreversibility of can only be traversed in the direction A→C→B→A.

## Slide 15: Analysis of an Irreversible Process
Suppose that both irreversible cycles are simultaneously possible, i.e., both cycles can be performed.
It turns out that if this is the case, then (AC) is false.
In effect, again, we approximate B to C in an arbitrary way.
As it was assumed that to be simultaneously possible, then as a consequence both irreversible processes A →B and A→C are also possible.

## Slide 16: Analysis of an Irreversible Process
Then, if C is approximated arbitrarily from B, and from A one can reach both B and C by irreversible adiabatic processe.
Therefore, from A all states on the same line x1∗--x2∗ as B and C can be reached by irreversible adiabatic processes.
Also approximate that the line x1∗--x2∗ arbitrarily close to A.

## Slide 17: Analysis of an Irreversible Process
It is obtained that:
arbitrarily close to A there are states that can be reached from A by irreversible adiabatic processes, thus falsifying (AC) for irreversible processes.

## Slide 18: Analysis of an Irreversible Process
Next is a routine step as done for reversible cycle.
In principle there is no physical argument that prevents (AC) from being false in the irreversible case.
Suppose that (AC) is really false and then are simultaneously possible.

## Slide 19: Analysis of an Irreversible Process
Then, repeating the argument for the reversible case and applying the first law of thermodynamics to both , it can be found that, at the end of each of these cycles

## Slide 20: Analysis of an Irreversible Process
For irreversible processes (KP) ⇒ (AC).

## Slide 21: Reversible Vs Irreversible Engines
Consider an irreversible cyclic heat engine operating between the same TH and TL as the reversible engine

## Slide 22
Irreversible and Reversible engines
LTR
QHER
QLER
ER
WnetR
Assume that an irreversible
Engine is more efficient than
the reversible engine.
QHEI
QLEI
EI
WnetI
QHE
QLE
E
WnetI
HTR

## Slide 23
For same Wnet, QHEI < QHER
Implies that, |QLEI | < |QLER|
But a reversible engine can be completely reversed and it will work as a heat pump.
Wnet,I Wnet,R
>
QHEI QHER
Let us construct a compound machine using an irreversible engine
and reversed reversible engine (reversible Heat Pump).
For same |Wnet |,
More Efficient Irreversible engine

## Slide 24: Compound Machine using Reversible & Irreversible Engines
LTR (Source)
HTR (Sink)
EI
QHPR
QLPR
R
WnetR
QHEI
WnetR
QLEI
For same |Wnet |,

## Slide 25: Compound Machine using Reversible & Irreversible Engines
LTR (Source)
HTR (Sink)
QHPR
QLPR
R
EI
QHEI
WnetR
QLEI
For same |Wnet |,

## Slide 26
QHPR
QLPR
QHEI
EI
R
WnetR
QHEI < |QHPR |
QLE
LTR (Source)
HTR (Sink)
|QLEI| < QLPR
QLPR - |QLEI |
|QHPR | - QHEI

## Slide 27: Irreversible Machines
The efficiency of an irreversible heat engine will always less than the efficiency of a reversible engine working between the same reservoirs.
The COP of an irreversible heat pump will always less than the COP of a reversible heat pump working between the same reservoirs.

## Slide 28: Further Discussions
hirr < hrev
1/hirr >1/hrev but, 1/hrev = brev
1/hirr > brev (Mathematically possible but thermodynamically impossible).
Similarly, birr < brev  1/birr > 1/brev
1/birr >hrev (Mathematically possible but thermodynamically impossible).

## Slide 29: Nature of Reversible Machines
For all reversible heat engines:
For all reversible heat pumps and refrigerators:
Therefore all reversible machines in this universe :

## Slide 30: Comparison of Reversible & Irreversible Engines
For a reversible engine with two adiabatic and two isothermal reversible processes:
= 0
Estimate this cyclic integral for a similar irreversible engine :

## Slide 31: Cyclic Analysis of Reversible Engines
For a reversible engine with two adiabatic and two isothermal reversible processes:
= 0
Reversible and irreversible are designed for same value of Wnet

## Slide 32: Cyclic Analysis Irreversible Engines
For same Wnet

## Slide 33: Comparison Cyclic Analyses
It is already known that

## Slide 34: Clausius Inequality
Therefore, all machines in this universe :
The fist step in consideration of the property we call entropy is to accept the inequality of Clausius,
The inequality of Clausius is a corollary or a consequence of the second law of thermodynamics.
It is valid for all possible cycles, including both reversible and irreversible heat engines and refrigerators.

## Slide 35: Entropy Change Of A Control Mass During An Irreversible Process
The cycle made up of the reversible processes A and B is a reversible cycle.
Therefore, we can write
The cycle made of the irreversible process C and the reversible process B is an irreversible cycle.
Therefore, for this cycle the inequality of Clausius may be applied, giving the result

## Slide 36
For reversible cycle 1A2B1:
Subtracting the second equation from the first and rearranging, we have
For reversible cycle 1C2B1:
Entropy Change Of A Control Mass During An Irreversible Process

## Slide 37
As path C was irreversible, the general result is:
Using the definition of entropy
Entropy Change Of A Control Mass During An Irreversible Process
For any process

## Slide 38
Above equation holds when dQ > 0, when dQ =0, and when dQ < 0.
If dQ is negative, the entropy of the system will tend to decrease as a result of the heat transfer.
However, the entropy of surroundings will tend to increase.
As a total the influence of irreversibility is still to increase the entropy of the system and surroundings.
Entropy Change Of A Control Mass During An Irreversible Process