## Slide 1
Design and Development of Water Wheels for Rural Energy Needs
Harvesting Energy Fruits out of Riverine Bounty …
P M V Subbarao
Professor
Mechanical Engineering Department
Head,CRDT

## Slide 2: Classification Hydro Power Plants : Capacity
Large- hydro More than 100 MW and usually feeding into a large electricity grid
Medium-hydro 15 - 100 MW - usually feeding a grid
Small-hydro 1 - 15 MW - usually feeding into a grid
Mini-hydro Above 100 kW, but below 1 MW; either stand alone schemes or more often feeding into the grid Micro-hydro
From 5kW up to 100 kW; usually provided power for a small community or rural industry in remote areas away from the grid.
Pico-hydro From a few hundred watts up to 5kW

## Slide 3: Layout of a Typical Micro/Pico Hydro Scheme
A Rural Set-up

## Slide 4: Samantara akSha-rekhA Jhal Chakra

## Slide 6: My First Exposure to Rural Needs: Native Energy System
Shri Mangal Singh
Water Wheel on River Sajnam, Bhailoni Lod Village
Lalitpur Dist.

## Slide 7: Photograph of Mangal Turbine

## Slide 8
Photograph of Mangal Turbine

## Slide 9
Photograph of Mangal Turbine

## Slide 10: Analysis of the Local Design
Diameter of the wheel : 4m.
Speed of the wheel: 13 RPM.
24 blades !
Huge Diameter !
Very Low Speed!
Weighing more than a ton!
Huge material cost!
The speed of A common pump or Generator is 1500 RPM.
A gear box is required to Increase the speed 120 times!
Very costly gear box.
Basic Limitation is Poor Blade Design

## Slide 11: Explanation by Shri Mangal Singh
We tried small wheels: They could not develop enough torque at all.
Large diameter produced enough torque to drive the pump.
Large diameter : Large Perimeter: More number of blades.
Result :Heavy and costly wheel !!!
Large diameter : Low RPM for same flow velocity.
Heavy and costly gear box.

## Slide 12: My Harsh Reaction
It is very non-scientific work.
Unreasonable design and cost.
One can decrease cost to one fourth, with little science and engineering.
!!!!!!!!
A Sponsored Project : 3.6 lakhs & One and Half years.
IIT Delhi design should be fabricated by same person and should be installed at same site.

## Slide 13: Site Analysis
Measure head and flow rate : h (in meters) & Q (in Cumecs).
Determine Hydropower.
Mechanical Power, Pmechanical
Decide various design factors of turbine For maximum efficiency.
Efficiency Achieved : 60 – 70%.
Select a suitable pump.
Design a suitable gearbox & Transmission system.

## Slide 15: Analysis of the Problem
Water is falling form a height H, called Head.
The velocity of the stream when reaches down most point is:
Newton’s Second Law applied for present problem:
Any Obstacle, which changes the direction of the steam (of given mass flow rate) will experience a force.
If the agent is fixed to a shaft, it can generate a torque.
The product of torque and speed of the agent is Power.

## Slide 16
Feasibility Constraint:
The peripheral Velocity of the wheel should be lower than the velocity of the water

## Slide 17: Scientific Model of The Turbine
1B
1C
2j
Rp
Re
d
dj, Vj
1A
1D
w

## Slide 18
Minimum Number of Buckets
q
y
Rp
Re
d
dj, Vj
lj
w
tj : Time taken bye the jet to travel lj
tb: Time taken by first bucket to travel
For better working tj < tb