## Slide 1
Atmospheric Boundary Layer & Micro Wind Turbines
P M V Subbarao
Professor
Mechanical Engineering Department
Head,CRDT
Advanced Sciences to Highlight the Superiority of Rural Sites for Wind Turbines

## Slide 2: Fundamental Force Fields responsible for Wind
Pressure gradient force
Viscous force
Gravitational force
Apparent forces: Centrifugal and Coriolis
Can you think of other classical forces ?
Would they be important in the generation and control of wind?
Electromagnetic force
Total Force field is the vector sum of all of these fields.

## Slide 3: The Momentum Equation of Real Wind
+ other forces
Pressure gradient force
Viscous force
Gravity force = gravitational force + centrifugal force
with g = 9.81 m s-2
Material derivative of the velocity vector

## Slide 4: Convection Cells in Earth’s Atmosphere

## Slide 5: Wind at Lower Altitudes
At heights in excess of 500m or so above the earth ‘s surface , horizontal air motions proceed in a largely geostrophic maner.
These motions are essentially unretarded by friction known as planetary boundary layer.
Between an altitude of around 50m and the surface , the speed of the wind reduces more and more rapidly towards zero .
This sub-region is often termed the ‘Surface Boundary Layer ‘.
The region between 500m and 50m is in effect a zone of transition between the smooth geostrophic flow in the free atmosphere and flow of an essentially turbulent nature near the ground.

## Slide 6: Variation of Wind Profiles and Superiority of Rural Sites
At lower altitudes the thickness of boundary layer is a strong function of surface roughness.
Rural locale
Urban locale
Sub-urban locale

## Slide 7: Instantaneous & Mean Wind Speed Profile
Day 1
Day 2
Day 3

## Slide 8: Random Nature of Wind
The wind in the atmospheric boundary layer is known to be distinctively turbulent and unsteady.
As a consequence the wind speed varies rather randomly on many different time scales.
These time scales range from long-term variations (years) to very short ones (minutes down to less than a second).
The latter are commonly considered to correspond to small-scale (microscale) turbulence.
These small-scale fluctuations are superimposed to the mean velocity varying on diurnal or even larger scales.

## Slide 9: Large Scale Wind Variations
Local Instantaneous Wind

## Slide 10: Characterization of Local Turbulent Wind
Mean velocity component
Turbulence Level

## Slide 11: A Model for Mean Wind Speed Profile
U* = friction velocity (m/s)
 = von Karman constant, approximately equal to 0.4
z = elevation above ground level (m)
z0 = empirical surface roughness length (m)

## Slide 13: Statistical Distribution of Turbulent Wind

## Slide 14: Two Variable (speed-direction) PDF for Wind

## Slide 15: PDF for Wind Speed
A single variable PDF can be generated using wind speed as a primary variable.
This function shows probability of occurrence of wind of a given speed in all possible directions.