## Slide 1
Design of Wind Turbine Rotors for RES
P M V Subbarao
Professor
Mechanical Engineering Department
Head,CRDT
Easy to Develop and Maintain Locally….

## Slide 2: The Cost of Wind Turbine

## Slide 3: The Power Extraction Analysis for Wind Turbines

## Slide 4: Mechanical Power Extraction :The Fundamental Aerodynamic Phenomena
All bodies exposed to an airflow experience aerodynamic force.
This force generated on a wind turbine rotor is responsible for
generation of change in tangential velocity across a rotor &
Axial induction in upstream wind.
The components of which are defined as
aerodynamic drag (in the direction of flow), and
as aerodynamic lift (at a right angle to the direction of flow).
The component of force responsible for above effects, greatly influences the actual power developed by a wind turbine.

## Slide 5: Basic Principle of Changing Angular Momentum/ Axial Induction
Drag driven WT
Lift driven WT

## Slide 6
Three Popular VAWTs
Vertical axis turbines (M. J. Khan et al. 2009)
Darrieus | Gorlov | Savonius
Types of vertical axis Wind turbines
Power Coefficient

## Slide 7
Parameter | Savonius | Gorlov | Darrieus
Power Coefficient | 0.15 - 0.2 | 0.35 | 0.4
Blade profile | Simple | Complicated | Complicated
Tip Speed Ratio | Low | Moderate | Moderate
Noise | Low | Low | Moderate
Blade area | Large | Low | Low
Self-starting | Yes | Yes | Yes, if helical
Overall structure | Simple | Complicated | Complicated
Manufacturing | Simple | Complicated | Complicated
Cost price | Low | High | High
Debris issue | Low | High | High
A Holistic Analysis of VAWTs

## Slide 8: Drag Translator
Drag results from the relative velocity between the wind and the device.
The power extracted by an elementary drag is the product of the drag force and the translation velocity.

## Slide 9: Simple Drag Device
The simplest type of wind energy conversion can be achieved by means of pure drag surfaces.
The air impinges on the surface A with velocity V0.
The instantaneous power capture P from the aerodynamic drag D, and the velocity Vblade with which it moves is expressed as :
Define coefficient of drag:
V0

## Slide 10: Capacity of Drag Device
Instantaneous Power Developed by a drag device
Average Power Developed by a drag device

## Slide 11: Power Coefficient of A multi-Cup Drag Wind Turbine
The instantaneous power coefficient of reference cup:
The instantaneous power coefficient of multi cup turbine:
The instantaneous torque coefficient of multi cup turbine:

## Slide 12: Savonius Rotor Wind Turbine

## Slide 13: Design of Blade for Savonius Rotor Wind Turbine

## Slide 14: Local Static Coefficient of Torque

## Slide 15: The cyclic torque coefficients with the time for modify 4 rotor at different

## Slide 16: Ensemble Average torque coefficient versus the instantaneous location of the rotor at different tip speed ratios.

## Slide 17: Savonius Turbine : Average Coefficient of Torque

## Slide 18: Savonius Turbine : Average Power Coefficient

## Slide 19
IIT Delhi : Savonius wind turbine
Advanced Savonius wind turbine

## Slide 20
Geometrical Variants of Savonius turbine